## Slide 1
S5 Error Budget
Presentation to SIP
Doug Lisman, Phil Willems
August 08, 2019

## Slide 2: Overview
A top level S5 error budget is presented herein that identifies all 8 of the Key Performance Paramters (KPPs) whose verification is the S5 focus
  Rolls up from a detailed error budget maintained by Stuart Shaklan (Shaklan et al, 2017 SPIE Vol 104001)
Instrument contrast drives 7 of the 8 S5 KPPs and is conservatively allocated at 1E-10 to not drive integration times
  Instrument contrast is defined as the energy ratio of the residual starlight at any point in the telescope focal plane relative to the starlight at the same point without the starshade
The S5 Error Budget is referenced to the WFIRST Rendezvous Mission but also carries reserve instrument contrast to address the HabEx Mission
  HabEx is slightly more sensitive to shape errors due to operating at 1.36 l/D IWA vs. 1.5 l/D
The S5 Error Budget carries large margins and a status is given
A top-down Monte Carlo analysis is also discussed

## Slide 3: Mechanical Shape Error Roll-Up

## Slide 4: S5 Top Level Error Budget
Flight dev. margin ≥100% margin
4 x 10-11
Study Circumstellar Disks
Study metallicity of Gas Giants
Limit photometric noise at IWA to ≤ 2-20X planet
Calibrate systematic noise to ≤ 1-10%
Detect & Characterize Earth 2.0
Planet/star flux ratio ≤ 4 x 10-11
Instrument Contrast
1 x 10-10
Mechanical Shape Error
2.1 x 10-11
Science investigations
Sunlight thru micrometeoroid holes
V > 31
(after multi-bounces)
Starlight thru micrometeoroid holes
0.1 x 10-11
Nominal specified shape
0.4 x 10-11
Solar Edge Scatter
V > 25 mags
in 2 lobes at IWA
Other stars
(galactic and extra-galactic)
V > 30
Solar Zodi
V > 29
per PSF at 760 nm
Reflected
bright bodies
V > 30
V> 32 99% of time
KPP 1
KPP 2
KPP 4
KPP 3
KPP 5
KPP 6
Lateral Formation Sensing ≤ ± 30 cm
Launch, cruise & non-thermal stability
0.1 x 10-11
Sunlight leakage thru optical shield flaps
V > 32
Exo-Zodi
V > 28
per PSF at 1.5X solar density
KPP
Threshold Values
Lateral Formation Control ≤ ± 1m
1 x 10-11
WFIRST-Starshade Rendezvous at 1.52 l/D IWA
Starshade
Background
Telescope
Model validation accuracy ≤ 25%
2 x 10-11
Verify in lab at subscale
(no hidden physics)
HabEx reserve at 1.36 l/D IWA
0.4 x 10-11
Allocated Instrument Contrast
3.6 x 10-11
Petal Shape
1.8 x 10-11
Petal Position
0.2 x 10-11
KPP 7
KPP 8
On-orbit thermal stability
≤ ± 200 µm
0.1 x 10-11
On-orbit thermal stability
≤ ± 80 µm
0.8 x 10-11
Pre-launch (Mfr., AI&T & storage)
≤ ± 300 µm
0.1 x 10-11
KPP Goals
Nominal CBE Values
Basis of estimate
≤ ± 50 µm
≤ ± 40 µm
TDEM-09 measurements
≤ ± 40 µm
≤ ± 20 µm
Unvalidated models
≤ ± 212 µm
≤ ± 170 µm
TDEM-10 measurements
≤ ± 100 µm
≤ ± 50 µm
Unvalidated models
25%
25%
100%
100%
Contingency or MUFs
Margin
41%
100%
100%
41%
Pre-launch (Mfr., AI&T & storage)
≤ ± 70 µm
1 x 10-11
Detector Noise
Read Noise:
Dark Current:
Cosmic Rays:
Time Variant

## Slide 5: S5 Error Budget Margins
Mechanical shape errors (KPP 5-8) are allocated large margins (allocated & unallocated)
One motivation to carry large margins was to cover uncertain performance of low-cost, readily available shape metrology systems (both room temp and over temperature systems)
But, our low-cost metrology is performing beyond expectation
We currently expect to not consume the margin

## Slide 6: Top-Down Monte Carlo Simulation
The error budget adds the nominal field separately and does not capture the mixing term between the nominal field and perturbations
  (Nominal + Perturbation)2 = Nominal2 + Perturbation2 + 2*Nominal*Perturbation
For this reason we conducted a top-down Monte Carlo (MC) simulation that includes all mixing terms in 2018
The MC simulation confirmed the mean value predicted by the error budget but shows a broader distribution
The MC result shows that we have 99% confidence to meet the allocated mechanical shape error with max expected errors (CBE + contingency) and 100% margin