## Slide 1: Retrieval of Aerosol Extinction Profiles from Limb Scattering Instruments: Experience with OMPS LP
P. K. Bhartia, Zhong Chen, Ghassan Taha
16.5 km
14.5 km
Evolution of Strat Aerosols from Aug 13, 2017 PyroCb
Notes: Simple 7 circuit Labyrinth. It is not a maze..

## Slide 2: Limb Scattering Instruments
SME: 1982-1988
SOLSE/LORE: 1997
SAGE III: 2002-2005, 2017-
SCIAMACHY: 2003-2011
GOMOS:2003-2011
OSIRIS: 2002-
OMPS: 2012-
Also flown on MARS missions

## Slide 3
Limb Scattering Technique
Line of sight
Tangent point
Tangent height
Diffuse upwelling radiation
Solar Radiation

## Slide 4: Suomi NPP O3 Monitoring & Profiler Suite (OMPS)
NP
NM
LP
Notes: OMPS consists of suite and ground processing algorithms
Two sensors, Limb and Nadir, provide Limb Profile, Nadir Total Column, and
Nadir Profile Raw Data Records
Main Electronics Boxes provide data processing, provide spacecraft electrical interfaces, and controls on-orbit operations
SDR and EDR algorithms process RDRs into SDR and EDR products
110° nadir cross-track field of view (FOV) and 3 limb FOVs provide required coverage
2.23° limb vertical FOV provides sampling from tropopause to 60 km

## Slide 5: LP Daily Coverage
Left slit can go to 85S

## Slide 6
OMPS LP Spectral Coverage/Resolution
30-65 km O3 and T
10-30 km O3
10-40 km aerosol extinction

## Slide 7: LS Aerosol Signal in SS Approx.
- O()
The 2nd term can cause to go to zero when is small and is large.
At any given l, Q and clouds determine the lower altitude cutoff. At 675 nm the cut-off varies from ~13 km in SH mid/high lat to cloud top in the tropics & NH.
Multiple scattering reduces the effect of phase function error.
Q
Dec 21
June 21
LP obs geometry

## Slide 8
Q
P(Q)
Pueschel et al.
CARMA
Pueschel
CARMA
Gamma vs Bimodal lognormal Size Distribution
0.1mm particle density seem to matter most for determining the phase function. Bimodal lognormal distributions tend to overestimate it when there are no measurements below 0.15mm.
Gamma distribution seems to produce more reliable results.

## Slide 9
Comparison with ISS/SAGE III
Improvement of stratospheric aerosol extinction retrieval from OMPS …….
Chen et al., submitted to AMT., amt-2018-221.
Green points: Bimodal LN distribution, parameters from aircraft meas
Blue points: Gamma distribution, parameters derived from CARMA model

## Slide 10: Key Conclusions
Based on a broad range of metrics the simple Gamma model does a better job for deriving aerosol scattering phase function than the bimodal lognormal model.
Unimodal lognormal works reasonably well, but it too over-predicts aerosol density below ~0.1 micron.
Gamma phase function and AE are well correlated, effectively making it a one parameter model for PF calculations.
The modified Gamma distribution may be needed if there are many coarse model particles.

## Slide 11
Time series (Jul 2016-Jun 2018) of aerosol extinction as seen by OMPS/LP at different altitudes

## Slide 12
SAGE III extinction profiles at 676 nm
OMPS/LP extinction profiles at 675 nm
Canadian PyroCb event was observed by LP and SAGE III/ISS

## Slide 13: Synergy with ISS/SAGE III
SAGE III measures aerosol extinction directly during solar/lunar occultation
  Comparison with LP can provide phase function information, which can then help tie down aerosol size distribution
SAGE III can also measure limb scattering between occultations at varying local times
  LS + occultation can better constrain aerosol size distribution, similar to AERONET DS + Almucantar data.
High spatial and temporal sampling from LP provides context to interpret SAGE data

## Slide 14: Relevant References
OMPS Limb Profiler Version 1 Aerosol Extinction Retrieval Algorithm: Theoretical Basis
  Loughman, Bhartia, Chen, Xu, Nyaku, and Taha.
  Published in AMT
Impact of aerosol size distribution on extinction and spectral dependence of radiances measured by the OMPS Limb profiler instrument
  Chen, Bhartia, Loughman, and Colarco.
  AMT discussions (under review, publicly available)
The sensitivity of the stratospheric aerosol phase function to aerosol size distribution models
  Nyaku, Loughman, Bhartia, Deshler, Chen, and Colarco.
  Under Revision