## Slide 1
SAGE III/ISS Science Team Meeting
NASA Langley Research Center
October 30-31, 2018

## Slide 2
Product Status: Introduction
D. Flittner

## Slide 3: INTRODUCTION
The next version of data products, Version 5.1 (Provisional), are targeted for public release after this meeting.
Key points of difference from V5.0 are:
  Retrievals to lower altitudes, generally;
  Revised wavelength calibration, hence slightly different effective cross-sections and resultant concentrations;
  Improved flagging of ISS structural blockages during data collections;
  Various errors corrected/bugs fixed/improvements in the transmission processing (Level 1b);
  Consistent computation of ozone uncertainty;
  Water vapor profiles
  File formats of HDF 5 or binary (HDF4-EOS format will not be available).
  NO2 absorption cross sections taken from Bogumil, et al.

## Slide 4: Standard Data Products: Provisional version, V5.1
# concentration; * Or cloud-top/ISS; ** at 600 nm
PRODUCT | Event Type | Vertical Range & Resolution [km] | Precision [%] | Accuracy Goal [%]
Spectral Transmission | Solar | 0* – 100, 0.75 | 0.1 | 0.1***
Aerosol Extinction & Optical Depth | Solar | 0* – 40, 0.75 | 5 | 5
Ozone# | Solar | 0* – 50, 0.75 | 5 | 5
Water Vapor# | Solar | 5* – 45, 0.75 | 10 | 10
Nitrogen Dioxide# | Solar | TP+2 – 45, 0.75 | 10 | 10
Ozone# | Lunar | 15* - 45, 1.5 | 5 | 6
Nitrogen Trioxide# | Lunar | 25 – 45, 1.5 | 15 | 10
Nitrogen Dioxide# | Lunar | 20 – 45, 1.5 | 10 | 10
Delayed
Beta