## Slide 1: Cloud Top Heights from SAGE III/ISS
J. Kummer, M. Schoeberl
STC
E. Jensen, R. Ueyama
ARC

## Slide 2: Outline
Review of our SAGE III cloud algorithm
Comparison to other observations
Future work

## Slide 3: How do we identify clouds within the SAGE III profiles?
2l algorithm, Thomason and Vernier (2013)
  Uses extinction ratio and extinction magnitude
  Can also be used with SAGE II
3l algorithm, Kent et al. (2007)
  Uses two extinction ratios
  Cannot be used with SAGE II

## Slide 4: Example of the 2l Algorithm
All TWP Points (2-λ)
x(z)=log10(β(z)1020)
z [km]
y(z)=β520 / β1020
> -3.7
< 2
Cloud
Lat/Lon: -21.45, 30.01
9/16/2017

## Slide 5: Same case for the 3l algorithm
All TWP Points (3-λ)
x(z)
y(z)
z [km]
Extinction Ratio [unitless]
Example of x~1 y~1 observation
Cloud
Lat/Lon: -21.45, 30.01
9/16/2017

## Slide 6: Case with an Aerosol Layer
All TWP Points (3-λ)
x(z)
y(z)
z [km]
Extinction Ratio [unitless]
Profiles of two color ratios
Cloud
Aerosols
Stratospheric Aerosols
Lat/Lon: 2.0, 150.55
4/24/2018

## Slide 7: Case with an Aerosol Layer
All TWP Points (2-λ)
x(z)=log10(β(z)1020)
z [km]
Profiles of extinction and color ratio
y(z)=β520 / β1020
Extinction increases while color ratio approaches 1
Cloud
Aerosols
Lat/Lon: 2.0, 150.55
4/24/2018

## Slide 8: Summary of the Two Techniques (June 2017 – March 2018 data)
Clouds
Clouds
Aerosols
Ratio 520/1020 threshold = 2
Log(1020 extinction) = -3.7
  3-λ (Kent)
  2-λ (Thomason)

## Slide 9: Final Cloud Algorithm
The two algorithms disagree where extinctions at 1020 and 1550 are small (basically dividing by a small number). To correct this we modify the Kent algorithm to include the Thomason extinction cutoff.
New Kent algorithm: A Cloud is detected if
  3-λ (Color Ratio (520/1020 and 1020/1550 ext.) is 0.75< CR < 2.0 for both ratios
  And Log10(1020 ext.) > -3.7 constraint from the 2-λ method.
The two algorithms now agree for 93% of the observations.

## Slide 10: Validating the SAGE III cloud algorithm with OMPS and CALIOP observations
Using all of the SAGE III, OMPS-LP, and CALIOP data available we compare
Zonal mean Cloud Top Heights (CTH)
Zonal Mean Difference of Cloud Top Heights Relative to OMPS-LP
Cloud Top Height Maps

## Slide 11: OMPS, SAGE and CALIOP Cloud Detection
CALIOP
SAGE III
OMPS LP
Extinction
Limb Scattering
Back scattering
Each system uses a different technique to identify cloud height.

## Slide 12: Zonal Mean CTH from SAGE III, OMPS-LP, CALIOP
km
Latitude
km
SAGE – OMPS
CALIOP – OMPS

## Slide 13: SAGE III Cloud Top Height (annual average)
km
TWP Clouds are higher than OMPS.
TEP Clouds are more consistent with OMPS

## Slide 14: Comparison to CALIOP and OMPS
SAGE III
OMPS
CALIOP
Overall, the three data sets are consistent
OMPS is ~1 km higher than CALIOP in TWP
SAGE III is slightly higher than OMPS in TWP
(1 year of data)
(7 years of data)
(5 years of data)

## Slide 15: Now look at JJA and DJF

## Slide 16: JJA 2017/18 Zonal Mean CTH from SAGE III, OMPS, CALIOP
Latitude
km
OMPS and SAGE III are very similar in the tropics
km
Differences

## Slide 17: SAGE III CTH JJA
SAGE III
OMPS
CALIOP
Overall, the three data sets are consistent
SAGE III and OMPS are closer
Some interesting differences
(2017/18)
(2017/18)
(2017/18)

## Slide 18: DJF 2017 Zonal Mean CTH from SAGE III, OMPS, CALIOP
Latitude
km
SAGE III is highest

## Slide 19
SAGE III CTH DJF
SAGE III
OMPS
CALIOP
Overall, three data sets are consistent
SAGE III is highest
Some interesting differences but more data is required
(2017)
(2017)
(2017)
(white means no data)

## Slide 20: Conclusions
Both algorithms 2l and 3l produce reasonable SAGE III Cloud Top Height. We use a modified 3l algorithm here (3lm).
Comparison with CALIOP and OMPS shows overall good agreement.
More SAGE data is required to solidify the comparisons and explore some of the differences.

## Slide 21: Future Work
Implement a cloud top height detection algorithm operationally.
The OMPS ‘radiance gradient’ cloud identification scheme could also be used with in SAGE III data – especially for SAGE III in limb scatter mode.
Computation of cloud fraction is an ongoing project
  Estimating cloud fraction is important for climate studies
  Converting the CALIOP viewing geometry to SAGE III/OMPS viewing geometry is a challenge since it re quires an assumption about the horizontal extent of clouds (e.g. Liao et al. 1995)