## Slide 1
Ground-Based Diurnal Measurements of NO2 and NO3 in Support of SAGE-III/ISS Validation
Thomas J. Pongetti1, King-Fai Li2, Yuk L. Yung3 and Stanley P. Sander1
1Jet Propulsion Laboratory, California Institute of Technology
2University of California, Riverside, 3Caltech
 2019, California Institute of Technology. Government sponsorship acknowledged.

## Slide 2
Objective 1: Obtain lunar occultation measurements of nighttime NO3 and NO2 from Table Mountain Facility in support of SAGE III/ISS validation.
Objective 2: Utilize in-situ measurements of NO3 and NO2 and chemical modeling to separate stratospheric and tropospheric partial columns.
Objective 3: Analyze comparisons with coincident SAGE III/ISS measurements and work with the Science Team to interpret the comparisons and incorporate improvements into retrieval algorithms.
Task Objectives
Co-Investigators | 
Thomas J. Pongetti, JPL | Data Acquisition/Analysis
King-Fai Li, UCR | 1-D Modeling
Yuk L. Yung, Caltech | 1-D Modeling
Steven S. Brown, NOAA | In-situ measurements

## Slide 3
Schematic of the instrument light path. (a) Light is collected by the primary of the heliostat (tracker) then through an off-axis telescope which also serves as a fine guider for the pointing system. (b) The light is directed through a condensing lens, shutter, order-sorting filter, and then into the spectrometer where it is dispersed and recorded by a CCD camera.
UV-Visible Grating Spectrometer at JPL/Table Mountain
Notes: Setup works for both solar and lunar occultation

## Slide 4
Heliostat for Solar and Lunar Occultation Spectroscopy
16 Primary Mirror
Equatorial Mount
10 Secondary Mirror
Fixed Mount
Fused Silica Isolation
Window
Notes: Large size driven because the heliostat is also feeding light to an interferometer with a large aperture.

## Slide 5
NO3 Spectral Fitting using the DOAS Approach
Raw spectrum with sloping baseline
High-pass filtered raw spectrum derived by
dividing the raw spectrum by a smoothed version
Differential spectrum after fitting solar, NO3, water vapor and O2 reference spectra
Residuals
Notes: Raw spectrum does not have obvious trace gas absorption features – dominated by Fraunhofer features

## Slide 6
Key Processes in Stratospheric NOx-NOy Photochemistry
Two pathways to HNO3 formation:
  Daytime (through OH + NO2 + M reaction)
  Nighttime (through N2O5 + sulfate aerosol reaction, NO3-mediated
Sensitive to Temperature
Sensitive to Pressure
Notes: Coupling of Nox cycle with HNO3 explains the diurnal variability of NO2 and NO3
NO3 is zero during the day due to rapid photolysis

## Slide 7
NO2 Diurnal Variation from Caltech 1-D Model
Vertical Profile and Total Column
Daytime increase driven by HNO3 + h
Nighttime decrease driven by NO2 + O3

## Slide 8
NO2 Vertical Column Data from Table Mtn.:
Diurnal View
Notes: First day+night measurements of NO2 and NO3, as far as I know.

## Slide 9
NO2 Seasonal Variability: Day/Night
Notes: Data reproduces the well-known stratospheric NO2 seasonal cycle

## Slide 10
NO2 Diurnal Variability: Model Comparison

## Slide 11
NO3 Vertical Column Data from Table Mtn.:
Diurnal View

## Slide 12
NO3 Seasonal Variability: Day/Night

## Slide 13
NO3 Diurnal Variability: Model Comparison

## Slide 14: NOAA NO3/N2O5 Instrument Installed at TMF on 16 October
2 Channel CRDS instrument was installed on the second floor of TM12, inlet was strung through the wall on the southwest side of the building
Notes: Instrument on loan from the Brown group at NOAA.

## Slide 15
NO3: Column (JPL)/Surface (NOAA)
First Results

## Slide 16
Occultation Events Near TMF
± 3° longitude, ± 1.5° latitude

## Slide 17
Summary
One year of data on NO2 and NO3 day and night column abundance data has been acquired.
Observed diurnal column data qualitatively agree with the Caltech 1-D model
Further analysis underway to quantify the effect of tropospheric NOx pollution on total columns
NOAA NO3/N2O5 instrument installed and running
A number of coincident measurements (mainly solar) with SAGE III/ISS have been identified and will be compared in the next year.