## Slide 1
Instrument Assembly
Samuel Porter

## Slide 2: Instrument Assembly
Science events
Azimuth motor health
Elevation motor health
Scan-plane alignment (off-nadir angle)
Dark current signal
Instrument response
CCD temperature stability

## Slide 3: Events (7/1/2017 - 10/23/2019)

## Slide 4: Azimuth Motor Current

## Slide 5: Elevation Motor Current

## Slide 6: Off Nadir Angle
Off nadir angle is the angle between the scan head and the nadir direction.
Level 1 science requires the scan head to be oriented within 1° of nadir during science events to ensure that the center of the Sun is being scanned tangentially to Earth’s limb.

## Slide 7
SAGE-III CCD

## Slide 8: SAGE-III CCD
Custom CCD with 8 segments which can be commanded individually to use different integration times as necessary.
CCD temperature is controlled with a thermal electric cooler (TEC) to reduce thermal agitation which decreases ambient charge or dark current.
  TEC nominally set to 12.5°C.
A photodiode is attached to measure 1550nm wavelengths (channel-9).

## Slide 9: Dark Current
TEC set to 13.5°C

## Slide 10: Channel-9 Response
Channel-9 response values are corrected to remove background noise.
Response values have decreased approximately 200 counts over 2 years.

## Slide 11: Blue Pixel Response

## Slide 12: Red Pixel Response

## Slide 13: TEC Efficiency
CCD Temp stabilized Nov. 2017

## Slide 14: TEC Efficiency

## Slide 15: Conclusion
Instrument Assembly is healthy and experiencing no major problems.
CCD pixel responses and TEC efficiency are showing no signs of degradation.
Some slight aging in the channel-9 photodiode response and dark current.
Improvements are being made to increase the amount of science data collected, and mitigate some causes of science event failures.