## Slide 1
SAGE III Limb Scatter Retrievals
Glen Jaross, P.K. Bhartia, Natalya Kramarova | NASA Goddard Space Flight Center
Ghassan Taha | Universities Space Research Association
Philippe Xu | Science Applications International Corp.
SAGE 3 STM, 30-Oct., 2019

## Slide 2
Provide LaRC operational retrieval codes that will work for SAGE LS data
  Ozone and aerosol extinction
  Based on existing OMPS retrievals
Correct Level 1 radiances for problems affecting product accuracy
  Stray Light: out-of-band and out-of-field
  Tangent Height registration errors
Recommend LS operations scenarios
  Optimize product quality and usefulness
Proposed effort

## Slide 3
OMPS LS retrieval algorithms
Aerosol v1.5 algorithm
Ozone v2.5 algorithm
Computes extinction profile at 675 nm;
Radiances are normalized at 40 km;
Gamma size distribution in Mie calculation;
Chahine’s non-linear relaxation algorithm;
Cut off at cloud top;
Residuals calculated at 8 wavelengths.
3 UV pairs and 1 VIS triplet;
Radiances are normalized at 55 km for UV and 40 km for VIS ranges (no retrievals above);
Include the explicit aerosol correction by using LP-derived aerosols;
Algorithm uses realistic a priori covariance matrices instead of Tikhanov regularization;
Limited wavelengths allow us to better isolate instrumental issues

## Slide 4
4 – 20 min. on day side
typically equatorial
two fast scans to 250 km
SAGE LS operations
Limb Scatter scan pattern
Wavelength (nm)
Sun-normalized signal
TOA Reflectance
We’ve been working with 2 orbits of 9 scans each
Notes: Scan head heats up after use, so operators desire to limit heating
Approximately one scan per minute

## Slide 5
Out-of-Field stray light is primary challenge
Telescope scatters bright Earth signal into higher altitude angles (in-band)
Excess signal at retrieval normalization altitude
Primarily a VIS/NIR problem
M3-SAGE LS Signal
M3-SAGE LS Signal

## Slide 6
Rayleigh residual=(Im-I0)/I0
where Im is the measured radiances and I0 is the calculated radiance for a Rayleigh atmosphere only.
OMPS has relatively little residual stray light
Assess stray light using Rayleigh residuals
Use wavelengths with little atmospheric absorption
OOF stray light is inherently worse at longer wavelengths due to greater vertical gradient in signal
OMPS residuals – Stray Light
( Percent )

## Slide 7
353 nm
508 nm
675 nm
Tangent Height (km)
Percent Residual
Ozone retrieval is not so bad due to wavelength triplet in VIS
UV
VIS
Tangent Height (km)c
O3 Density × 1012 (cm-3)
SAGE LS Rayleigh residuals
Suggests large levels of stray light

## Slide 8
How best to correct for stray light ?
Empirical Fit Method
Mirror scatter function deconvolution
Radiance Signal
Tangent Height (km)
Fit Range
Predicted Stray Signal
675 nm
TH diff from direct signal (km)
Fractional Contribution
Lorentzian + constant
Multiple wavelengths shown
Radiance Signal
Tangent Height
675 nm
Each method requires tuning to “truth”
OR

## Slide 9
60%
40%
30%
15%
8%
Lots of stray light !
Modeled stray light as a percent of useful signal across VIS ozone range
Typical SL corrections achieve only a 10x reduction

## Slide 10
There are significant differences, but hard to say which method is better
Post-correction Rayleigh residuals
Radiance Fit Method
Percent Residual
Tangent Height
Mirror Scatter Method
Percent Residual
Tangent Height
353 nm
508 nm
675 nm

## Slide 11
Radiance Fit Method
Mirror Scatter Method
Sample retrieved ozone profiles
Data are adjusted for TH errors based on the RSAS technique
Comparisons to coincident OMPS measurements
Tangent Height
Tangent Height
O3 Density × 1012 (cm-3)
O3 Density × 1012 (cm-3)
Percent Difference
Percent Difference
UV
VIS

## Slide 12
Radiance Fit Method
Mirror Scatter Method
Two orbits (18 scans) have been processed
Ensemble difference vs. OMPS
Percent Difference
Percent Difference
Tangent Height
Tangent Height
UV
VIS

## Slide 13
SAGE aerosol extinction (675 nm) compared to OMPS
Backward Scatter Orbit
Forward Scatter Orbit
Backscatter retrievals are more sensitive to radiance errors such as stray light
Extinction Coeff. (km-1)
Sample scan
9 scan comparison
Tangent Height (km)
Extinction Coeff. (km-1)
Sample scan
9 scan comparison
Tangent Height (km)
Notes: Backscatter example neither best nor worst

## Slide 14
Radiance Fit Method
Mirror Scatter Method
Forward scatter extinction profiles
Most scans are equally good for two techniques
Comparisons to coincident OMPS measurements
Tangent Height
Tangent Height
Tangent Height
Tangent Height
Extinction Coeff. (km-1)
Extinction Coeff. (km-1)

## Slide 15
Summary
SAGE stray light is a significant limitation
Difficult to tune stray light correction to work well for both ozone and aerosols
Forward scatter aerosol retrievals show most promise
Path Forward
Process data coincident with SAGE occultation
Concentrate LS operations on forward scattering
Begin work on production processing