## Slide 1
Thierry Leblanc, Fernando Chouza
and the JPL-TMF Lidar Tech Team:
M. Brewer
D. Koon
P. Wang
Jet Propulsion Laboratory, California Institute of Technology
Wrightwood, CA USA
Validation of SAGE-III/ISS Ozone and Aerosol Profiles
Using the JPL Lidars at Table Mountain Facility, CA
and Mauna Loa Observatory, HI

## Slide 2
Ozone DIAL Principle
1. Two laser beams of different wavelengths are sent in the atmosphere
1
3
2
4
2. Light is backscattered by molecules and particles
3. Light is collected in optical channels
4. Signals are sampled as a function of time (i.e., altitude)
DIfferential Absorption Lidar

## Slide 3
Ozone DIAL Retrieval
5. One beam is more absorbed by ozone than the other beam
Ozone Number Density is computed from the difference of signal slope at the two wavelengths
5

## Slide 4
JPL Stratospheric Ozone Lidars Quick Facts
Mauna Loa stratospheric Ozone DIAL (MLSOL):
- Emitter uses 2 excimer lasers (308 nm) and 1 Nd:YAG laser (355 nm)
- 6-channel receiver : - Rayleigh 308/355 nm, high intensity, for z > 30 km - Rayleigh 308/355 nm, low intensity, for z < 35 km - Raman 332/387 nm, z < 35 km
- Retrieved species: - Ozone, 15-50 km, effective vertical resolution: 0.5 to 4 km - Temperature, 15-90 km , effective vertical resolution: 0.5 to 2 km - Aerosol backscatter, 15-50 km , effective vertical resolution: 0.5 to 2 km
Table Mountain stratospheric Ozone DIAL (TMSOL):
- Instrumentation and design similar to MLSOL
- 4-5 nighttime profiles per week
- Same retrieved species as MLSOL
- 3-4 nighttime profiles per week
- Full dataset covers period 1993 – Present
- Full dataset covers period 1988 - Present

## Slide 5
1999-2017 average
In 2018
What’s new since 2018: TMF Lidars Upgraded
Automation:
More measurements, any day, any time
 Now easier to get measurements for ALL SAGE-III/ISS coincident events
Very-near range channel on Tropo DIAL:
Now covering altitudes down to 90 m a.g.l.
Full O3 column, ground to 50 km, using combination  of surface, UAV, tropo. DIAL and strato. DIAL
Chouza, F., et al., 2019: Atmos. Meas. Tech., http://doi.org/doi:10.5194/amt-12-569-2019

## Slide 6
Courtesy of Wolfgang Steinbrecht
Ozone and Temperature Long-term Records at TMF and MLO
Stratospheric ozone
Temperature
Contribute to the ground-based datasets used for the assessment of long-term trends

## Slide 7
Comparisons with SAGE-III/ISS
Products
- Lidar: GLASS v1 O3 ND (new data processing for NDACC, to be archived 2019)
- SAGE-III/ISS AO3 v5.1 O3 ND, all event types (SR, SS, lunar)
- Aura-MLS v4.2 O3 VMR converted to ND (vs. geom. alt.) using MERRA-2 P/T
- For MLO only: Hilo ozonesonde O3 PP converted to ND using sonde T
Coincidences:
SAGE-III/ISS: All occultation events within 1000 km of lidar sites and +/- 12 hours
Aura-MLS: All profiles within 1000 km of lidar sites and +/- 12 hours
Ozonesondes: All Hilo profiles within +/- 12 hours

## Slide 8
Lidar vs. SAGEIII-ISS, MLS and ozonesonde (O3)
Lidar vs. SAGE-III/ISS mean difference: ~ 5% between 20 and 45 km

## Slide 9
Lidar vs. SAGEIII-ISS, MLS and ozonesonde (O3)
Lidar vs. SAGE-III/ISS mean difference: ~ 3% between 20 and 40 km

## Slide 10
SAGE-III/ISS is now the reference
SAGEIII-ISS vs Lidar, MLS and ozonesonde (O3)
Within reported total uncertainty in most cases
All instruments within 5% between 20 and 45 km
Exception below 20 km (cf. discussions on O4 dimer/extinction)

## Slide 11
Aerosols

## Slide 12
Aerosol Retrieval
Rayleigh channels impacted by aerosol backscatter, Raman channels NOT impacted
 Ratio of 355 / 387 L1B signals provides aerosol backscatter

## Slide 13
Aerosol Extinction Coefficient above MLO
MLSOL Lidar backscatter coefficient at 355 nm converted to 532 nm using å = 1.6
MLSOL Lidar extinction coefficient computed from backscatter using L = 50 sr
SAGEIII/ISS
CALIOP L3
GLOSSAC
MLSOL Lidar
PyroCb 2017
Raikoke

## Slide 14
Stratospheric Aerosol Optical Depth above MLO
Generally good agreement between lidar, GLOSSAC, CALIOP L3, and SAGE-III/ISS
CALIOP L3 systematically higher than the others
SAGE-III/ISS below lidar in 2017, then above lidar
Strong lidar signature of Raikoke volcanic eruption in Sept. 2019, possibly enhanced by active fire season in Siberia

## Slide 15
Raikoke Elevated Plume
At 18 km
https://www-calipso.larc.nasa.gov/tools/data_avail
CALIPSO Attenuated backscatter coefficient, July 14, 2019

## Slide 16
At 26 km
https://www-calipso.larc.nasa.gov/tools/data_avail
CALIPSO Attenuated backscatter coefficient, September 23, 2019
Raikoke Elevated Plume

## Slide 17
26 km and rising….
Plume trajectory derived from CALIPSO backscatter coefficient, orbit-by-orbit visual inspection
Journey starts in the Aleutian Highs (3 weeks residence there?)
Plume circled NP 3 times before its detection at MLO on September 24
https://www-calipso.larc.nasa.gov/tools/data_avail
7 km rise in 2 months (late July to late Sept.)

## Slide 18
Raikoke Plume Impact on Ozone
Right plot (Ozone): Plume affects Rayleigh channels (blue)
Raman channels (green) must be used to retrieve proper ozone below 28 km
 First critical use of MLSOL’s Raman channels since Pinatubo era!
Left plot (Backscatter coefficient): Plume detected at MLO on Sept. 24 and Sept. 26 at around 26 km altitude

## Slide 19
Conclusion / Future Plans
2017-2019 comparisons SAGE-III/ISS AO3 vs. JPL Lidar O3 at MLO and TMF show 3-5% agreement for altitudes 20-45 km (SAGE-III high)
Quite good considering low number of coincidences
 Looking forward to next data processing version, with UTLS issues resolved…
JPL Lidars not limited to MLO and TMF stratospheric DIAL
THANK YOU
2017-2019 lower stratosphere turned out to be quite “dirty”
 Next validation efforts will involve TMF Tropo O3 DIAL, TMF Water vapor Raman lidar, and temperature...