## Slide 1
Status of Oxygen A-Band Temperature/Pressure Research Products
Michael Pitts

## Slide 2: Strategy for Temperature/Pressure Retrievals
Iterative approach required due to non-linear nature of problem
Uses non-linear least squares fitting routine (Levenberg-Marquardt)
  Simultaneously fits measured A-band spectra from all 14 channels and 90 tangent altitudes
    Includes O2 absorption, Rayleigh scattering, aerosol extinction, and O3 absorption components
  Solves for successive adjustments to trial T,p profiles by minimizing residuals between measured and modeled absorption
  Includes non-rigid hydrostatic constraint
A-band contains ~290 individual absorption lines with the distinctive R-branch and P-branch structure. Broad features are still visible at SAGE III resolution (red line)
14 Channels at ~ 1-nm intervals
FWHM ~ 1.4 nm
SNR ~ 1500

## Slide 3: Forward Model Elements
Forward model simulates SAGE III/ISS LOS transmission measurements in 14 O2 A-band channels using LBL radiative transfer calculations
Inputs:
  Initial guess T/p profiles
  Pathlength matrix
  O2 Spectroscopic parameters (HITRAN 2016)
  Initial guess aerosol (linear fit: slope + intercept)
  Initial guess ozone (cross sections + ozone number density)
  Channel wavelength map
  Channel point spread function (PSF)
Outputs
  LOS transmission (O2 + Rayleigh + aerosol + O3)
A-band contains ~290 individual absorption lines with the distinctive R-branch and P-branch structure. Broad features are still visible at SAGE III resolution (red line)
14 Channels at ~ 1-nm intervals
FWHM ~ 1.4 nm
SNR ~ 1500
PSF
FWHM

## Slide 4: Baseline Retrievals (Sunrise Events)
Mean SAGE III/ISS retrieved temperature and pressure profiles from 30 sunrise events during March 2018 with baseline wavelength map and PSF widths
~50º-55º N latitude
First Guess
MERRA2/GRAM95
SAGE III

## Slide 5: Baseline Retrievals (Sunset Events)
Mean SAGE III/ISS retrieved temperature and pressure profiles from 30 sunset events during March 2018 with baseline wavelength map and PSF widths
~5º-30º S latitude
First Guess
MERRA2/GRAM95
SAGE III

## Slide 6: Measured vs. Modeled O2 + Rayleigh Components
Baseline wavelength registration and instrument response functions
Modeled spectra too broad and misregistered in wavelength

## Slide 7: Wavelength and PSF Factor Adjustments
Assume MERRA2/GRAM95 T/p profiles are truth
Retrieve adjustments (mean ± 1 s) to baseline wavelength map and PSF widths required to best fit measured spectra
Channel PSF
FWHM
100
45

## Slide 8: Retrievals Using Adjusted Wavelength & PSF
Mean SAGE III/ISS retrieved temperature and pressure profiles from 30 sunrise events during March 2018 with adjusted wavelength map (-0.018 nm) and PSF factor (0.95)
~50º-55º N latitude
First Guess
MERRA2/GRAM95
SAGE III

## Slide 9: Retrievals Using Adjusted Wavelength & PSF
Mean SAGE III/ISS retrieved temperature and pressure profiles from 30 sunset events during March 2018 with adjusted wavelength map (-0.063 nm) and PSF factor (0.95)
~5º-30º S latitude
First Guess
MERRA2/GRAM95
SAGE III

## Slide 10: Aerosol and Ozone Fitting
Retrieved aerosol and ozone components compared with measurements (aerosol interpolated from standard aerosol channels and ozone from AO3 ozone product)

## Slide 11: O2 + Rayleigh Fitting
Mean measured vs. modeled O2 absorption + Rayleigh scattering for 30 SS events
Forward model parameters:
Dl = -0.063
PSF Factor = 0.95
Systematic shape of residuals may indicate that some component is not being properly fitted

## Slide 12: Summary and Future Work
Forward Model Assessment:
  Small wavelength shifts are apparent in A-band spectra relative to baseline registration (approximately -0.018 nm for sunset and -0.063 nm for sunrise events)
  Baseline PSFs too broad- fits are improved using narrower (0.95 x baseline) widths
Retrievals with adjusted forward model parameters look encouraging with near science quality temperature products, but some issues remain, especially in pressure products
Future Work:
  Continue examining sensitivity to forward model parameters
    Bandpass (width, wings, etc.)
    Spectroscopy (line intensities, line shape)
    Potential altitude offset
    Aerosol + O3 components
  Exclude weaker channels at higher altitudes
  Explore alternative retrieval approaches to L-M (e.g., Newton-Raphson)
  Perform more detailed comparisons with correlative measurements (e.g.,radiosondes, lidar, MLS, and global analyses) to better quantify precision and accuracy of T/p products

## Slide 13: SAGE III/ISS vs. Merra-2 zonal cross sections
MERRA-2 (left) and SAGE III/ISS (right) meridional temperature distributions compiled from sunrise events over the period 1 January -15 February 2018. The SAGE III/ISS temperature distribution captures the general temperature structure seen in MERRA-2, but is colder at the tropopause and stratopause, and somewhat noisier at higher altitudes.
MERRA-2
SAGE III/ISS