## Slide 1
Observatory Reference Information
Nancy Grace Roman Space Telescope
March 1, 2021

## Slide 2: Roman Mission Key Characteristics
Mission Life: 5 years (+ ~3 month checkout)
Mission Orbit: Sun-Earth L2
Baseline Launch Vehicle: Falcon Heavy, New Glenn, Vulcan possible
Observatory:
  2.4 m primary mirror Telescope
  Wide Field Instrument (WFI)
  Coronagraph (CGI)
  S/C Bus
    Downlink Rate & Volume – 250-500 Mbps, 11 Tbits/day
    Pointing stability: 8 mas drift, 12 mas jitter, RMS per axis
  Refuelable in flight
Ground System:
  Ground Stations: NEN-White Sands, NM; ESA-New Norcia, Australia; JAXA – GREAT, Japan; DSN
  Operations: GSFC, STScI, IPAC

## Slide 3: Observatory Overview
Key Features
Telescope: 2.4m aperture
Instruments:
  Wide Field Imager / Slitless Spectrometer
  Internal Coronagraph
Data Downlink: 250-500 Mbps
Data Volume: 11 Tb/day
Orbit: Sun-Earth L2
Launch Vehicle: 3 options
Mission Duration: 5 yr, 10yr goal
Serviceability: Observatory designed to be robotically refuelable

## Slide 4: Observatory Expanded View
Deployable Aperture Cover (DAC)
Outer Barrel
Assembly (OBA)
Solar Array
Sun Shield (SASS)
Spacecraft Bus Avionics Panels
Propulsion Module
Communications
Module
Wide Field
Instrument (WFI)
Coronagraph
Instrument (CGI)
(outer enclosure
not shown)
Instrument
Carrier (IC)
Imaging Optics Assembly
Observatory = Spacecraft + Integrated Payload Assembly
Spacecraft Bus
Integrated Payload
Assembly

## Slide 5: System Architecture Diagram
Mission Operations
Center (MOC)
Science Operations Center (SOC)
Flight Dynamics Operations Area (FDOA)
Science Users & Community
SITs, Public
GO/GI, PSP
Archive
Science Support Center (SSC)
Planning & Scheduling Products
CGI HK Data
Maneuver Plans, Products
NEN: S-Band (CMD/TLM/TRK); Ka-Band (SCI)
ESA-New Norcia: Ka-Band (SCI)
JAXA-GREAT: Ka-Band (SCI)
DSN: S-Band (CMD/TLM/TRK)
HK Telemetry
Science Data Files
Observatory Commands
Acquisition and Tracking Data
CMD – Command; TLM – Telemetry; TRK – Tracking; HK – Housekeeping; SCI – Science
SN (Launch Support):
S-Band (CMD/TLM)
Coronagraph Technology Center (CTC)
CGI Commands & Products
WFI & SOSE Data Products
Observation Planning,
Data Products
Observations,
Data Products
Observations,
Data Products, Proposals
CGI Observations,
Data Products
DAPHNE

## Slide 6: Field of Regard
SNe Fixed Fields ±20˚ off the Ecliptic Poles
Microlensing can observe Inertially Fixed Fields in the Galactic Bulge (GB) for 72 days twice a year
HL/GO/Coronagraph Surveys can be optimized within the full Observing Zone
Observing Zone:
54˚-126˚ Pitch off SunLine
360˚ Yaw about Sun Line
±15˚ Roll about Line of Sight (LOS) off max power roll angle
Earth/Moon LOS avoidance angles are a minor sporadic constraint
+54˚
Keep-Out
Zone
Observing Zone
Keep-Out
Zone
SNe Fields
SNe Fields
+126˚
Galactic Bulge (Available twice yearly)
GB

## Slide 7: Payload Optical Block Diagram

## Slide 8: Optical Field Layout

## Slide 9: Representative Slew Times
Slew type | Slew angle (deg) | Slew time (s) 6 wheels | Slew time (s) 5 wheels
Gap Fill | 0.025 | 21.4 | 23.4
Short FoV | 0.4 | 49.3 | 54.8
Long FoV | 0.8 | 67.4 | 76.0
2-deg | 2.0 | 98.7 | 116
5-deg | 5.0 | 162 | 179
10-deg | 10.0 | 267 | 284
30-deg | 30.0 | 667 | 684
90-deg | 90.0 | 1865 | 1882
Times computed assuming maximum expected inertia.
Times shown include the settle time.
Baseline operations:
6 wheels
Must meet mission requirements with 5 wheels

## Slide 10: Slew and settle times