## Slide 1: A Decade Plus of Discovery – Observing a Changing Moon with the Lunar Reconnaissance Orbiter
NASA’s Goddard Space Flight Center
Notes: -This presentation combines three slide decks originally given by Noah Petro, John Keller, and Andrea Jones. Additional content has been added to include updates as of September 2022.
-Noah Petro is the Project Scientist for the Lunar Reconnaissance Orbiter mission.
-John Keller is the former Project Scientist for the Lunar Reconnaissance Orbiter mission.
-Andrea Jones is the Lunar Reconnaissance Orbiter Education and Public Outreach Lead.

## Slide 2: Lunar Reconnaissance Orbiter (LRO)
NASA's Scientific Visualization Studio
Notes: -Image credit: NASA’s Scientific Visualization Studio
-LRO was launched in June 2009 from Cape Canaveral, FL.
-LRO has generated the largest volume of data of any planetary body.
-LRO has 6 instruments & 1 technology demonstration  https://lunar.gsfc.nasa.gov/instruments.html; https://www.nasa.gov/mission_pages/LRO/spacecraft/index.html
-LRO is helping to pave the way for future human exploration of the Moon through NASA’s Artemis missions.
  LRO data is critical for identifying Artemis landing sites and can be used to support other aspects of Artemis.
-LRO’s Science Objectives:
Investigate:
  Impact history of the Moon
  Lunar geologic processes and their role in the evolution of the lunar crust
  Formation of the lunar regolith (soil)
  Volatiles on the Moon, especially at the poles
  Lunar radiation environment

## Slide 3: LRO Exploration Objectives
Locate potential resources
  Water at the lunar poles?
  Continuous source of solar energy
  Mineralogy
Space environment
  Energetic particles
  Neutrons
New technology
  Advanced radar
Safe landing sites
  High resolution imagery
  Global maps
    Topography
    Rock abundances
Notes: -Image credit: NASA

## Slide 4: Launch!
June 18, 2009
Arrived at the Moon 4.5 days later
3 months commissioning (instrument check-out)
Initial 50-km polar mapping orbit
Sister spacecraft: LCROSS
Pat Corkery, United Launch Alliance
Notes: -Image credit: Pat Corkery, United Launch Alliance  https://www.lroc.asu.edu/posts/145
-More on LCROSS: https://www.nasa.gov/mission_pages/LCROSS/overview/index.html

## Slide 5: LRO’s Instruments
Notes: -Image credit: NASA/GSFC/Arizona State University
  The central peaks of Plaskett crater rise more than 6500 feet (about 2000 meters) above the shadowy crater floor. An image from NASA’s Lunar Reconnaissance Orbiter.

## Slide 6: LOLA: Lunar Orbiter Laser Altimeter
Uses laser pulses to characterize topography, slope, and surface reflectance
Can identify areas of permanent sunlight and shadow through analysis of surface elevations
Notes: Supports:
Detailed characterization of the lunar surface
Identify resources - sunlight
Identify landing hazards, such as rough terrain or rocks
https://lunar.gsfc.nasa.gov/lola/

## Slide 7: LROC: Lunar Reconnaissance Orbiter Camera
Visible, UV, and infrared imagery
High resolution camera
Images help characterize the surface, identify resources and hazards, and provide polar illumination data
Notes: High resolution camera can resolve objects down to 1m in diameter.
Supports:
Detailed characterization of the lunar surface
Identify resources - sunlight
Identify landing hazards, such as rough terrain or rocks
https://www.lroc.asu.edu/

## Slide 8: Diviner Lunar Radiometer Experiment
Measures surface and subsurface temperatures
Identifies cold traps and potential ice deposits
Identifies landing hazards, such as rocky terrain
Helps determine surface composition
Notes: https://www.diviner.ucla.edu/

## Slide 9: LAMP: Lyman Alpha Mapping Project
Measures reflected UV radiation from distant stars
“Sees inside” permanently shadowed craters
Notes: https://www.boulder.swri.edu/lamp/index.html

## Slide 10: LEND: Lunar Exploration Neutron Detector
Measures the flux of neutrons from the Moon
Identifies potential ice deposits
Notes: Measures likely hydrogen concentrations, which indicates likely water concentrations (expect in form of water ice)
https://np.cosmos.ru/

## Slide 11: CRaTER: Cosmic Ray Telescope for the Effects of Radiation
Measures incoming radiation (solar, cosmic background, and reflected lunar radiation)
Contains a human Tissue Equivalent Plastic to assess biological impacts of radiation
Notes: https://crater.unh.edu/

## Slide 12: Mini-RF Technology Demonstration
Measures reflectivity using X and S band radar
Can identify likely ice deposits
Can “see” beneath the surface
Supplements visible imagery
Notes: https://www.nasa.gov/mission_pages/Mini-RF/main/index.html

## Slide 13: Science Results
Notes: -Image credit: NASA/GSFC/Arizona State University
  The central peaks of Plaskett crater rise more than 6500 feet (about 2000 meters) above the shadowy crater floor. An image from NASA’s Lunar Reconnaissance Orbiter.

## Slide 14: Near and Far Side Images of the Moon
NASA/GSFC/ASU
Notes: -Image credits: NASA/GSFC/Arizona State University  http://lroc.sese.asu.edu/posts/707
  The LRO Camera imaged the entire Moon in great detail!
  Note how different the near side (left image) and far side (right image) of the Moon look. We still don’t know why they look so different. We have some ideas, but we’re not sure yet.

## Slide 15: Topographic Map of the Moon
NASA/GSFC/DLR/ASU
Notes: -Image credit: NASA/GSFC/DLR/ASU  This color-shaded relief view of the Moon’s far side, taken by NASA’s Lunar Reconnaissance Orbiter, is part of the highest-resolution near-global lunar topographic map ever created.
  The blues and the purples are lower parts of the Moon while the reds and whites are higher mountainous parts.
  The giant purple region in the south is called the South Pole-Aitken basin and is the largest impact basin on the Moon.
    Its diameter is roughly 2,500 km (1,550 mi) which means that it stretches over nearly a quarter of the Moon (this translates to roughly the height of the contiguous U.S.)!
-We can now determine slopes of all major geologic terrains on the Moon at 100-meter scale.
 Current radial accuracy of the LOLA global topographic model is <1 m and the spatial accuracy of the lunar geodetic grid is ~30 m.
-We also know the topography of the Moon better than the Earth (since the Earth has oceans).
(https://www.lpi.usra.edu/meetings/lpsc2011/pdf/2350.pdf)

## Slide 16: Shrinking Moon
NASA/GSFC/ASU/Smithsonian
Notes: -Image credit: NASA/GSFC/ASU/Smithsonian
-Contraction causes the lunar crust to be pushed together, breaking the near-surface materials. The result is a steep slope on the surface called a scarp.
-Left image: A fault scarp cut across and deformed several small diameter (~40m) impact craters (arrows) on the flanks of Mandel’shtam crater (6.5°N, 161°E). The fault carried near-surface crustal materials up and over the craters, burying parts of their floors and rims. About half of the rim and floor of a 20m in diameter crater shown in the box has been lost. Since small craters only have a limited lifetime before they are destroyed by newer impacts, their deformation by the fault shows the fault to be relatively young.
-Right image: A thrust fault pushed crustal materials up the side of Gregory crater (2.1°N, 128.1°E). White arrows indicate the fault scarp.
-Scientists have found hundreds of previously undetected scarps in LRO images. LRO Camera (LROC) data have shown that many of the newly discovered scarps formed much less than a billion years ago, and they could be as young as 50 million years!
-The scarps are found globally, making a shrinking Moon the most likely explanation for their wide distribution.
-For more info: https://www.nasa.gov/mission_pages/LRO/news/shrinking-moon.html

## Slide 17: Shrinking Moon
NASA/GSFC/ASU
Notes: -Image credit: NASA/GSFC/Arizona State University
-The Moon is shrinking as its interior cools, getting more than about 150 feet (50 meters) skinnier over the last several hundred million years. Just as a grape wrinkles as it shrinks down to a raisin, the Moon gets wrinkles as it shrinks. Unlike the flexible skin on a grape, the Moon’s surface crust is brittle, so it breaks as the Moon shrinks, forming “thrust faults” where one section of crust is pushed up over a neighboring part.
-The shrinking of the Moon is also generating Moonquakes!
  https://www.nasa.gov/press-release/goddard/2019/moonquakes

## Slide 18: Likely Locations of Early Molten Moon’s Deep Secrets
NASA/LRO/Lunar Prospector/D. Moriarty
Notes: -Image credit: NASA/LRO/Lunar Prospector/D. Moriarty  The thorium concentration across the vast South Pole – Aitken Basin on the lunar farside reveals the distribution of mantle materials violently ejected during the basin-forming impact.
  Here, thorium abundance is represented by a rainbow color scale, with high-thorium areas shown in red, trending to purple and grey with lower abundances.
  Two craters in the northwestern region of the basin exhibit especially high thorium abundance (indicated in red on the map), suggesting the presence of abundant mantle materials currently exposed on the surface.
-The Lunar Reconnaissance Orbiter (LRO) is NASA’s flagship mission at the Moon, and it’s been orbiting the Moon for over 10 years! LRO is building on the legacy of Apollo, reshaping our understanding of our nearest neighbor in space – revealing an unexpectedly dynamic world right beside our own. And, it’s helping us prepare for the next phase in human exploration of the Moon through the Artemis program.
-Using data from LRO, Lunar Prospector, and the Moon Mineralogy Mapper instrument on board India’s Chandrayaan-I spacecraft, scientists have identified likely locations for NASA’s Artemis missions to find and collect pieces of the Moon’s mantle.
-For years, scientists have been puzzled by a radioactive anomaly in the northwest quadrant of the South Pole – Aitken Basin on the lunar far side. The team’s analysis demonstrates that the composition of this anomaly is consistent with the “sludge” that forms in the uppermost mantle at the very end of magma ocean crystallization. Because this sludge is very dense, scientists have previously assumed that it should completely sink into the lower mantle early in lunar history.
  But, recent models and experiments indicate that some of this sludge gets trapped in the upper mantle, and later excavated by this vast impact basin. So, this northwest region of the South Pole – Aitken Basin is the best location to access excavated mantle materials currently on the lunar surface.
-The precious rocks born deep within the Moon can help us understand how our Moon and other rocky worlds evolved.
-More info: https://www.nasa.gov/feature/goddard/2021/lro-deep-secrets-of-moon

## Slide 19: North Pole Temperatures
NASA/GSFC/UCLA
Notes: -Image credit: NASA/GSFC/UCLA  Left: Maximum daytime temperatures of the north pole of the Moon, as measured by the Diviner instrument onboard LRO. Right: Minimum daytime temperatures of the north pole of the Moon, as measured by the Diviner instrument onboard LRO.
-The Diviner Lunar Radiometer (DLRE) instrument provides orbital thermal mapping measurements, giving detailed information about surface and subsurface temperatures (identifying cold traps and potential ice deposits), as well as landing hazards such as rough terrain or rocks.
-The spin axis of the Moon is almost perpendicular to the ecliptic plane. The result is that areas of high and low elevation at the lunar poles experience extremes in illumination, with some crater floors remaining in permanent shadow.
-Diviner has revealed that temperatures within these permanently shadowed craters can fall as low as 25K (-414.4°F). For comparison, Pluto is about -234°C (-390°F). These cold traps present ideal candidates for potential stores of ice on the lunar surface because although the Moon has no indigenous water, molecules are deposited on its surface from comet and asteroid impacts.
-With the exception of Mercury, the Moon has the most extreme surface thermal environment of any planetary body in the solar system.
-At the lunar equator, mean surface temperatures reach almost 400K (260.6°F) at noon and then drop to below 100K (-279.4°F) during the night. For comparison, the mean surface temperature on Earth is a temperate 295K (71.6°F).
-For more info on Diviner: https://www.diviner.ucla.edu/science

## Slide 20: Improvements to Impact Crater Science
NASA/GSFC/ASU
Notes: -Image credit: NASA/GSFC/Arizona State University  http://lroc.sese.asu.edu/posts/384
  LROC NAC oblique view of Tycho crater; highlights the summit area of this spectacular image.
  The central peak complex is about 15 km wide southeast to northwest (left to right in this view).
  The crater is 86 km in diameter, 4.8 km deep.

## Slide 21: Large Moon Boulder
NASA/GSFC/ASU
Notes: -Image credit: NASA/GSFC/Arizona State University  http://lroc.sese.asu.edu/posts/384
  Boulder at the top of this mountain is the size of a baseball stadium!
  And, we have no idea how it got there! Our current impact cratering models do not permit it to be there. Images like this have revolutionized our understanding of impact crater formation.

## Slide 22: Chappy Crater
NASA/GSFC/ASU
Notes: -Image credit: NASA/GSFC/Arizona State University  http://lroc.sese.asu.edu/posts/899
  Chappy crater (1400 m diameter) is a very young impact crater whose ejecta spreads out more than ten diameters from the crater.
  This image really gives you a sense of the power and the forces involved in creating impact craters. Also – the Moon was impacted more frequently than we realized before we began monitoring with LRO. All of this bombardment breaks up the lunar surface, producing lots of broken rock and dust called regolith.

## Slide 23: Recent Volcanism
NASA/GSFC/ASU
Notes: -Image credit: NASA/GSFC/Arizona State University  https://lroc.sese.asu.edu/posts/818
  Interpreted as evidence of recent volcanism – possibly less than 50 million years old. Before the Lunar Reconnaissance Orbiter, most scientists thought volcanism ended on the Moon *billions* of years ago, so this is really recent! Changes how we think about lunar evolution – it might be that the interior of the Moon is hotter than we thought.
    The end of lunar volcanism took place more than a billion years ago. Or did it? Over sixty small patches of very young volcanic flows were discovered in LROC images. These small extrusions of basaltic material, similar to lava being erupted in Hawaii, are known as Irregular Mare Patches, or IMPs, and were erupted in the past 10 to 100 million years.
    The most famous IMP is Ina-D (shown in this image) and was known from Apollo era images. The smooth blobs inside the volcanic crater (caldera; 1800 meters wide) have very few impact craters on them testifying to their young age. How young are they? Only a returned sample will tell us!

## Slide 24: Illumination Maps
Notes: -Image source: http://lroc.sese.asu.edu/exhibits/A%20New%20Moon%20Rises/41
  This is an illumination map of the Moon’s South Pole. The illumination maps illustrate what percent of a year each pixel is in sunlight. Some peaks are illuminated for more than 80% of the time while areas of permanent shadow appear black.
  We are using maps like this to decide where to land for future human Moon missions, and where to build a lunar base.
    We are combining this with lots and lots of additional data from other instruments onboard the Lunar Reconnaissance Orbiter and other spacecraft – including upcoming lunar cubesats. We want to make sure we go to the Moon safely, and to areas of rich scientific interest.

## Slide 25: Explore the Lunar South Pole!
1.8 km
(1.1 miles)
2.1 km
(1.3 miles)
South Pole Illumination Map
Illuminated for 94% of the year
Longest eclipse is 43 hours
As low as -407°F in cold traps
Constant -64°F in sunlight
Notes: -More info: http://lroc.sese.asu.edu/posts/991

## Slide 26: Water ice on the Moon
Notes: -Image credit: NASA/GSFC  LRO observations indicate that Cabeus, Shoemaker, and Faustini craters show great potential for containing subsurface ice – these craters are located near the lunar South Pole. (https://svs.gsfc.nasa.gov/11756; https://svs.gsfc.nasa.gov/4057)
-LRO looks for water using its Lunar Explorer Neutron Detector (LEND) instrument, which detects the presence of hydrogen atoms by counting neutrons released from the Moon’s soils. The measurements allow scientists to create maps that show areas of the Moon that are rich in hydrogen, the main ingredient of water.
-When galactic cosmic rays strike atoms in the lunar soil (regolith), some neutrons get knocked off. These neutrons bounce from atom to atom like billiard balls, losing energy with each collision. Along the way, some of these neutrons escape into space, where LEND can detect them. The presence of hydrogen in the lunar soil reduces the number of neutrons that escape.
-To map out likely deposits of water ice, LEND scientists look for this deficit of neutrons in the epithermal (medium) energy range.
-Since LRO’s launch in 2009, the mission has identified likely deposits of water ice in a handful of craters on the Moon’s south pole, including shadowy regions (permanently shadowed regions) that have gone without sunlight for millions or even billions of years.
-LEND and other missions have found signs of water in places that aren't permanently shadowed while apparently excluding some places that are, both of which are surprising and exciting discoveries.
-LEND also provides space radiation environment measurements useful for future human exploration.
-For more info on LEND: https://np.cosmos.ru/pribory/lend
-More info on water on the Moon: https://moon.nasa.gov/inside-and-out/water-on-the-moon/

## Slide 27: Resource Potential of Permanently Shadowed Regions
Brown et al., 2022, Icarus
Notes: -Source: Brown et al., 2022, Icarus
  Resource potential for volatiles (group of chemical elements and chemical compounds that can be readily vaporized; e.g., nitrogen, carbon dioxide, hydrogen, water) in lunar permanently shadowed regions (PSRs).
  North (left) and South (right) Pole PSR volatile ranking thematic maps overlaying Diviner annual maximum bolometric temperature (Paige et al., 2011; Williams et al., 2019).
  Blue PSRs have observations of volatiles strongly consistent with water ice in multiple datasets, while orange PSRs are inconsistent with water ice or have a low signal-to-noise ratio (SNR), inhibiting the interpretation of water ice.
  PSRs in green have observations of volatiles that are inconsistent between datasets or show a limited potential area consistent with water ice.

## Slide 28: Lunar Pits
Safe havens for astronauts?
NASA/GSFC/ASU
Notes: -Image credit: NASA/GSFC/Arizona State University  http://lroc.sese.asu.edu/posts/286
-The LRO Camera (LROC) Narrow Angle Camera (NAC) acquired an oblique view of the Marius Hills pit with just the right angle to reveal an overhang! Pit is about 65 meters in diameter.
-Since LRO completes a full cycle of lunar imaging each month, it is possible to follow up previous discoveries and re-image targets under different lighting conditions. The LROC team waited patiently until the Sun and orbit position in the Marius Hills region was such that the bottom of the previously imaged pit wall was illuminated at just the right angle so that if there was an open lava tube extending horizontally its floor would be illuminated. The spacecraft slewed 43° to the east and the solar incidence angle was 34° from vertical.
-In this geometry, the NAC was able to image a few meters under the overhang discovering a sublunarean void.
-Also note how the oblique angle really brings out the layered nature of the mare bedrock in the pit walls. These exposed layers give scientists important clues as to how the vast mare were deposited.
-More on lunar pits: http://lroc.sese.asu.edu/posts/228 & http://lroc.sese.asu.edu/posts/230

## Slide 29: Lunar Pits
Mare Tranquillitatis pit
Pit diameter: 100 m
Pit depth: 107 m
Notes: -Image credit: Ashley, J & S. Robinson, M & Ray Hawke, B & Boyd, A & Wagner, Robert & J. Speyerer, E & Hiesinger, H & van der Bogert, Carolyn. (2011). Lunar Caves in Mare Deposits Imaged by the LROC Narrow Angle Cameras.  https://www.researchgate.net/publication/234129963_Lunar_Caves_in_Mare_Deposits_Imaged_by_the_LROC_Narrow_Angle_Cameras
-Mare Tranquillitatis pit: top left: near-nadir image, top right: 7° emission angle image; collectively reveal more than 90 percent of the floor - both images are approximately 175 m wide.
-Bottom left: oblique view (26° emission angle)
-Bottom right: Schematic showing Marius Hills cave in cross-section with viewing geometry for direct observing under the surrounding mare. A similar situation is shown in bottom left image for the cave in Mare Tranquillitatis. The dotted lined portion of this void space is speculative.

## Slide 30: New Impacts!
NASA/GSFC/ASU
Notes: -Image credit: NASA/GSFC/Arizona State University
-More on new lunar impact craters: https://www.nasa.gov/content/goddard/nasas-lro-spacecraft-finds-march-17-2013-impact-crater-and-more

## Slide 31: Repeat Imaging of Apollo Landing Sites
17
15
12
14
16
11
NASA/GSFC/ASU
Notes: -Image credits: NASA/GSFC/Arizona State University
  LRO takes images of the Apollo landing sites every time it passes over them.
  Near side (left image): http://lroc.sese.asu.edu/posts/707
  Far side (right image): http://lroc.sese.asu.edu/posts/298

## Slide 32: Apollo 12 Landing Site
NASA/GSFC/ASU
Notes: -Image credit: NASA/GSFC/Arizona State University  http://lroc.sese.asu.edu/posts/401
  The Apollo 12 landing site in Oceanus Procellarum as imaged by LRO’s Narrow Angle Camera (NAC).
  HGA: High Gain Antenna
  PLSS: Portable Life Support System backpacks

## Slide 33: Apollo 11 Landing Site
NASA's Scientific Visualization Studio
Notes: -Video credit: NASA’s Scientific Visualization Studio  https://svs.gsfc.nasa.gov/4185
  The Apollo 11 landing site as visualized using LROC data.
  Taking LRO data and recreating Apollo landing sites from a flyover perspective.

## Slide 34: Traces from Apollo 17
NASA/GSFC/ASU
Notes: -Image credit: NASA/GSFC/Arizona State University
-This image of the Apollo 17 landing site was taken by the Lunar Reconnaissance Orbiter Camera.
-You can see the astronauts’ footprints, rover tracks, and equipment.

## Slide 35: Where is LRO now?
LRO continues to serve the science and exploration communities of NASA, commercial entities, and international partners.
Notes: -The LRO mission is in its fifth extended science mission phase with an emphasis on supporting Artemis, the Commercial Lunar Payload Services (CLPS) program, as well as partner international space agencies.
-LRO has been extended to operate until at least October 2025!
-LRO continues to collect new data to support the Commercial Lunar Payload Services (CLPS) landing site characterization.

## Slide 36: Science in LRO’s 5th Extended Mission
Volatiles and external interactions
Interior, volcanism, and tectonics
Regolith and impacts
Programmatic support
Notes: -Image credit: NASA/GSFC
-Volatiles and External Interactions:
  Temporal coverage over Cabeus crater will be excellent in LRO’s 5th extended science mission (ESM5), allowing scientists to revisit the LCROSS impact results.
  Extreme temperature changes and areas coming into sunlight after extended periods in shadow may drive volatile migration, which scientists will be able to learn more about in LRO’s ESM5.
-Interior, Volcanism, and Tectonics:
  Surface changes identified through temporal imaging may be associated with activity along faults. New images for detection of low-relief landforms will be acquired in LRO’s ESM5 to help better understand the Moon’s interior structure.
-Regolith and Impacts:
  Temporal imaging enables the identification of surface changes (new craters), differences in regolith (lunar soil) exposed in new crater ejecta, as well as new targets for space weathering studies. Only a spacecraft in orbit at the Moon for extended periods of time can build this set of self-consistent data. These features become targets for all instruments.
-Programmatic Support:
  A host of missions are slated to go to the lunar surface during LRO’s ESM5. LRO will support landing site characterization, new product development, and coincident science measurements during operations for both landed and orbital missions. Researchers are at a unique moment in lunar science where they can connect surface measurements to simultaneous orbital measurements.
-More: https://svs.gsfc.nasa.gov/14171

## Slide 37: Fun Discoveries from LRO
The Moon is changing, and we can watch it!
Some regions are really cold (-414.4°F)!
Lunar pits as possible safe havens for astronauts
The Moon may have been geologically active very recently (for a geologist…)
Notes: -Image credit: NASA/GSFC/Arizona State University
-Changes: volatile movement, new impact craters, lunar tides, shrinking Moon!
-A temperature of -414.4°F (-248°C) was found on the floor of Hermite Crater (near the lunar north pole). These temperatures are among the coldest surface temperatures measured in the solar system, colder even than Pluto.
-Lunar pits: could be used as safe havens for astronauts.
-Geologic activity could have happened in the last 100s of millions of years!

## Slide 38: Learn More & Get Involved!
Notes: -Image credit: NASA/GSFC/Arizona State University
  The central peaks of Plaskett crater rise more than 6500 feet (about 2000 meters) above the shadowy crater floor. An image from NASA’s Lunar Reconnaissance Orbiter.

## Slide 39: International Observe the Moon Night
Linda McKenna
Sylvain Bouley/ASPA
Victoriano Canales Cerdá
Gunstar Team
Joaquin Zurdo
Zach Tejral
#ObserveTheMoon
moon.nasa.gov/observe
BRAZIL
ANTARCTICA
SPAIN
Yvelice Castillo
HONDURAS
PANAMA
UNITED STATES
SENEGAL
Notes: International Observe the Moon Night is a worldwide celebration of lunar science and exploration, celestial observation, and our cultural and personal connections to the Moon. Every autumn, we invite everyone on Earth to observe, learn about, and celebrate the Moon together. People participate in a variety of ways, including hosting or attending virtual or in-person events and observing the Moon from home. Participants also connect online with fellow lunar enthusiasts around the world through our social media platforms.
Learn more and register on the program website: https://moon.nasa.gov/observe.

## Slide 40: LRO on the NASA Website
https://www.nasa.gov/LRO
Notes: See the latest visualizations from the LRO visualization team, the latest press releases of LRO science results, and more!
https://www.nasa.gov/LRO

## Slide 41: LRO Camera Website
https://lroc.sese.asu.edu
Notes: Find images, data, where LRO is now, and more on the Lunar Reconnaissance Orbiter Camera website: https://lroc.sese.asu.edu

## Slide 42: MoonTrek
https://trek.nasa.gov/moon/
Notes: Explore Earth’s nearest celestial neighbor using this interactive website. Perform a wide range of analyses such as measuring distances, creating elevation plots, and conducting lighting and slope analysis. You can also draw bounding boxes around any areas of interest to generate output files for 3D printing of desired surface features.
https://trek.nasa.gov/moon/

## Slide 43: Resources
Moon:
  https://moon.nasa.gov
  https://lunar.gsfc.nasa.gov/education.html
  http://lroc.sese.asu.edu/educators/activities
General:
  NASA’s Scientific Visualization Studio: https://svs.gsfc.nasa.gov/
  NASA’s Solar System: https://solarsystem.nasa.gov/
  NASA’s Solar System Treks: https://trek.nasa.gov/
  NASA Solar System Resource Packages: https://solarsystem.nasa.gov/resource-packages/
Notes: -Image credit: NASA  A Station 1 pan from the first EVA of Apollo 15, showing Hadley Rille on the left and Mt. Hadley on the right.