## Slide 1: Apollo 15
Presenter’s name
Presenter’s title/position
Notes: -Image credit: NASA  A Station 1 pan from the first EVA of Apollo 15, showing Hadley Rille on the left and Mt. Hadley on the right. The image frames are ID: AS15-85-11400 and 11404  https://www.hq.nasa.gov/alsj/a15/a15north1221435dmh.jpg
-For mission patch image, see https://history.nasa.gov/apollo_patches.html
-Tips:
  You do not need to use everything in this presentation!
  Feel free to alter/edit this presentation to fit your specific needs/audience
-If you have any questions, please contact presentation author Staci Tiedeken (staci.l.tiedeken@nasa.gov, NASA GSFC)
-Updated January 2023

## Slide 2
Notes: -NASA press releases (July 1971): https://historydms.hq.nasa.gov/sites/default/files/DMS/e000041737.pdf

## Slide 3
Notes: -NASA press releases (July 1971): https://historydms.hq.nasa.gov/sites/default/files/DMS/e000041736.pdf

## Slide 4: Overview
July 26-August 7, 1971
David R. Scott
Alfred M. Worden
James B. Irwin
Notes: -Image credit: NASA  Apollo 15 crew. From left: David Scott (commander), Alfred Worden (command module pilot), and James Irwin (lunar module pilot).
-Fourth human Moon landing – Scott and Irwin landed on the lunar surface on July 30, 1971 at 6:16pm EST, with the first extravehicular activity beginning on July 31 at 9:13am EST.
-Apollo 15 was the first of the so-called J missions, which considerably expanded the capabilities for doing science on and near the Moon.
  For the first time, three 7-hour-long EVAs would be performed, and a lunar rover would significantly extend the distance a crew could travel over the lunar surface. In addition, the restriction on landing near the equator was lifted. Finally, a sophisticated suite of science experiments was also carried in the service module and used to map the Moon from orbit.
-The mission plan for Apollo 15 had several objectives for the crew to accomplish: survey and sample materials and surface features in a preselected area of the Hadley-Apennine region, emplace and activate surface experiments, evaluate the capability of the Apollo equipment to provide extended lunar surface stay time, and conduct inflight experiments and photographic tasks from lunar orbit.
-David Scott was the mission commander and was the pilot of Gemini 8, command module pilot on Apollo 9, and backup commander of Apollo 12.
-Alfred Worden was the command module pilot and was the backup command module pilot for Apollo 12.
-James Irwin was the lunar module pilot and was the backup lunar module pilot for Apollo 12.

## Slide 5: Launch
Launch
Notes: -Image credits: NASA (https://history.nasa.gov/afj/ap15fj/01launch_to_earth_orbit.html)
-The 363-foot-tall Apollo 15 space vehicle was launched from Pad A, Launch Complex 39, Kennedy Space Center, at 9:34 a.m. EDT on July 26, 1971.
-More about the launch: https://history.nasa.gov/afj/ap15fj/01launch_to_earth_orbit.html

## Slide 6: Launch
Launch
Larry Summers
Larry Summers
Notes: -Image credits:
Right: Larry Summers (https://richesmi.cah.ucf.edu/omeka/items/show/5989)
  A crowd estimated at 20,000 people parked along Kennedy Parkway North at John F. Kennedy Space Center (KSC) in Merritt Island, Florida, to observe the Apollo 15 launch on July 26, 1971.
Left: Larry Summers (https://richesmi.cah.ucf.edu/omeka/items/show/5976)
  The crowds of spectators observing the launch of Apollo 15 near the Vehicle Assembly Building (VAB).
-As with the previous Apollo crewed missions, adjacent to Kennedy Space Center (~3.5 miles away), thousands of spectators camped out on beaches and roads to watch the launch of Apollo 15.
-Apollo 15 launched in the morning due to considerations of the lighting at the time of the lunar landing and the time of flight from launch to landing.

## Slide 7: Saturn V Size Comparison
Notes: -Image credit: NASA  1967 illustration compares the Apollo Saturn V spacecraft (363 ft) of the Moon Landing era to the Statue of Liberty (305 ft).
-A Saturn V rocket has 3 stages, 11 powerful rocket engines, and huge tanks for kerosene (RP-1) and liquid hydrogen and oxygen. It’s still the largest crewed rocket ever flown and the only one to carry humans beyond Earth orbit.
  Height: 111 meters (363 feet)
  Diameter: 10 meters (33 feet)
  Mass: 2,840,622 kg (6,262,500 pounds) at liftoff (about 100 fully loaded tractor-trailers – only 1% of this actually goes to the Moon)
  Maiden Flight: Nov. 9, 1967 (uncrewed)
  The rocket generated 34.5 million newtons (7.6 million pounds) of thrust at launch, creating more power than 85 Hoover Dams.
  Could launch about 43,500 kg (50 tons) to the Moon (about the same as 4 school buses).
  The Apollo 15 launch vehicle was the tenth in the Apollo Saturn V series and was the eighth crewed Saturn V vehicle.
  More info on Saturn V: https://solarsystem.nasa.gov/news/337/what-was-the-saturn-v/

## Slide 8: Apollo Spacecraft Design
Apollo Spacecraft
Engine Bell
Thrusters
High-Gain Antenna
Thrusters
Thrusters
Descent Stage
Ascent Stage
Command Module
Service Module
Falcon Lunar Module
Endeavour
Notes: -Image credit: NASA  Diagram of the combined Apollo command and service module/lunar module translunar coast configuration.
-The lunar module was named Falcon while the command module was named Endeavour for Apollo 15.
-Source: https://history.nasa.gov/afj/ap13fj/04day1-end.html

## Slide 9: Apollo 12 Landing Site
Moon on July 30, 1971
Notes: -Image credit: NASA's Scientific Visualization Studio  The top-most green dot marks the site of the Apollo 15 landing on the eastern margin of the Imbrium Basin. The left-most green dot represents the Apollo 12 landing site, in Oceanus Procellarum (“Ocean of Storms”), and the green dot next to Apollo 12’s landing site is that of Apollo 14 which landed in the Fra Mauro formation. Apollo 11’s landing site in Mare Tranquillitatis is shown as the green dot at the far right.
-The Apollo 15 landing occurred on the eastern margin of the Imbrium Basin in the region known as Palus Putredinis (“Marsh of Decay”) at 6:16pm EST on July 30, 1971.
-A first quarter Moon phase was chosen since the terminator was reasonably close to the landing site.
  This meant that the Sun would be behind the lunar module as it came in for landing. This provided the most favorable lighting conditions to enable the astronauts to better discern and avoid craters, because the craters would have more elongated shadows.
  It also kept the surface temperatures at a reasonable level once the astronauts got outside, since it was effectively “lunar morning.”

## Slide 10: Overview
Marsh of Decay
Notes: -Image credit: NASA  Image ID: AS15-M-1537
  This frame was taken on August 1, 1971 at 15:38 UTC; it shows an oblique view of the landing site at bottom center (white arrow) and, at the upper left, craters Autolycus and Aristillus.
-The landing site chosen for Apollo 15 was on the eastern margin of the Imbrium Basin in the region known as Palus Putredinis (“Marsh of Decay”). This is one of the most geologically significant sites on the Moon.
  The site is nestled between the towering Apennine mountains, attaining heights of 3-5 km (~10,000-16,000 ft), and the 200 m (~650 ft) deep v-shaped valley of Hadley Rille.
  Notable features of the Apennine Mountain Range include Mons Hadley, Mons Hadley Delta and the Swann Range.
-There were two main objectives for this landing site:
  First, the rim of the Imbrium Basin could be sampled along the Apennine Mountains. It was expected that this would provide material from deeper in the lunar crust than was sampled in the Fra Mauro formation by Apollo 14.
  Second, this site provided an opportunity to explore Hadley Rille, a photogenic channel in the mare surface that was probably formed by volcanic processes.

## Slide 11: Overview
A Firm Landing
Tilted Falcon
Notes: -Image credit: NASA  Image ID: AS15-86-11600; note the dramatic tilt of the spacecraft.
-To prepare for their missions, Apollo crews were heavily trained to recognize specific large-scale lunar surface features at or near the designated landing site. These features would help the astronauts find their way to a safe area as close to the planned landing site as possible. But sometimes, lighting conditions would conspire with local topography to deceive even the most highly-trained eye.
  The astronauts trained with a model of the landing site (https://www.hq.nasa.gov/alsj/a15/a15SiteModel.html), but the craters of the model were a little too deep (they didn’t have the incredible data that NASA’s Lunar Reconnaissance Orbiter has been collecting since 2009), so the shadows on the model were much more pronounced than they were on the Moon during landing.
  With 2 min left on the descent of the lunar module (LM) Falcon, Dave Scott looked out his window and could not find the sequence of four craters as a visual guide to his planned landing spot northwest of the fourth and final crater, Index. Said Scott during a 1971 Technical Debrief: “When we pitched over, I couldn’t convince myself that I saw Index crater anywhere.”
    Falcon came to rest with its rear footpad on the rim of a 20-foot-wide crater. This caused one of the lunar module’s footpads to be off the surface entirely and placed the spacecraft at an 11-degree tilt. Stated Scott in the mission’s debrief: “…at the altitudes looking down as we approached the landing, it was very difficult to pick out depressions… as far as the shallow depressions there and the one in which the rear footpad finally rested, I couldn’t see that they were really there. It looked like a relatively smooth surface.”
-More from the 1971 Technical Debrief:
  At touchdown, the astronauts’ descent rate was 6.8 feet per second, and they were drifting north at 1.2 ft/s and west at 0.6 ft/s. A quick calculation using descent rates of 0.5 feet per second at contact and 6.8 feet per second at touchdown indicates that Scott got the engine off at an altitude of about 4.3 feet and that they had a free-fall time of about 1.2 seconds.
    Estimates of the vertical speed at touchdown on 5 of the 6 Moon landings: Neil Armstrong’s was the lowest at 1.7 ft/s because he didn’t get the engine shutdown until after the footpads were on the surface. On Apollo 12, 14, and 17, the landing speeds were all between 3.0 and 3.5 ft/s. Dave Scott’s was by far the highest at 6.8 ft/s, most likely because he was the fastest to hit the engine stop button and, therefore, fell the farthest.
    The engine cutoff before the LM’s legs were on the surface was intentional on all Apollo landings in order to keep dust from getting into the descent engine – the legs were designed to absorb the shock though.
    Both the drop and the tilt of the LM on Apollo 15 were within the LM’s specs.
  Dave Scott, recalling the landing: “Yeah, we hit firm. And one of the reasons - and Jim and I talked about it after we got down - of course, is that you don’t know how it’s going to feel when you land on the Moon until you land on the Moon. So I don’t know what the other guys...I’ve never looked at the acceleration on touchdown. I don’t know how to compare it. But it was a firm touchdown. One reason was, remember, we had to get the engine off. So, by golly, as soon as we got the contact light, the engine goes off. Another reason is we were the heaviest LM, so we’re going to fall harder (but not faster) once we get the engine shut down. And another reason was we landed in that little crater, so when we touched down, we touched down probably one foot and then the other foot into the crater. So it was a firm landing, and Jim was probably surprised, not expecting it. I’m expecting it, because I’m flying it. And it’s, again, the guy in the front seat versus the guy in the back seat. The guy in the front seat is tuned to what’s going on, and the guy in the back seat isn’t. So he’ll be somewhat behind in the event. So what Jim was saying was ‘Wow, we really had contact’.”
  More commentary: https://history.nasa.gov/alsj/a15/a15.landing.html#1044248
  Commentary on damaged engine bell (at 119:57:14): https://www.hq.nasa.gov/alsj/a15/a15.lrvdep.html

## Slide 12: Overview
Surveying the Landscape
Notes: -Image credit: NASA  https://www.hq.nasa.gov/alsj/a15/a15.hadleydelta_dmh.jpg  A partial Stand-Up EVA pan showing a dramatic view of the Apennine Front.
-Two hours after touchdown, Scott opened the hatch at the top of the lunar module Falcon and took a series of camera shots to get a panoramic view of the site (this was called the Stand-Up EVA or SEVA).
    Scott, his upper body extending through the top hatch of the lunar module (LM), performed the 33-minute Stand-Up EVA, and from this elevated vantage point, described the lunar terrain, used the Sun compass to establish the location of the LM with respect to recognizable lunar features, and obtained panoramic photographs of lunar terrain and photographs of interesting distant features.
-Unlike the other Apollo crews, Apollo 15 astronauts Dave Scott and Jim Irwin chose to sleep after their landing instead of exploring the Moon by foot right away. By resting right after landing, the crew was able to preserve their energy for the longer mission. Scott did, however, perform a Stand-Up EVA before heading to sleep.
-Link to Apollo 15 Stand-Up EVA video created by NASA Goddard: https://www.youtube.com/watch?v=O8WhmRvEEME

## Slide 13: Pete Conrad stepping on the lunar surface
“Exploration at its greatest.”
Notes: -Video credit: NASA ; link to video: https://www.hq.nasa.gov/alsj/a15/a15.lrvdep.html (video clip just after 119:54:42 in the surface journal).
  As Dave Scott’s boots come into view, he is hopping from rung to rung with his feet together, undoubtedly guiding himself with his hands. As he hops down to the footpad, he lets his hands slide down the outer rails of the ladder and then, letting go of the ladder with his left hand, steps off the footpad and rotates to his left as he looks off to the northwest. After a few seconds, he releases his right hand and turns to his right and appears to look up at the spacecraft.
  119:55:42 Joe Allen (EVA CapCom): Dave, an extraordinary television picture here.
  119:55:45 Scott: Okay, Houston. As I stand out here in the wonders of the unknown at Hadley, I sort of realize there’s a fundamental truth to our nature. Man must explore. (Pause) And this is exploration at its greatest. (Long Pause as Dave moves away from the TV camera) Well, I see why we’re in a tilt. (Pause) We’ve got...(Laughs) That’s very interesting. There’s so much hummocky ground around here (that) we’re on a slope of probably about 10 degrees. And the left-rear foot pad is probably about 2 feet lower than the right-rear foot pad. And the left-front’s a little low too. But the LM looks like it’s in good shape. The Rover’s in good shape.

## Slide 14: Pete Conrad coming down the ladder from the lunar module
Lunar geology studies
Lunar sample collection
Lunar surface science experiments
Orbital science experiments
  Lunar-focused
  Space environment-focused
Science-focused Mission
Notes:       -Image credit: NASA  Here, Jim Irwin salutes the American flag while standing beside the lunar module and rover.
-In addition to their geologic studies, the Apollo 15 crew performed several experiments on the lunar surface. The results of some of these experiments were either radioed to Earth by the crew or returned to Earth for laboratory analysis. Other experiments were deployed by the crew and then monitored from Earth by radio telemetry after the crew departed. This group of experiments was termed the Apollo Lunar Surface Experiment Package (ALSEP).
  Soil Mechanics Investigation
  Solar Wind Composition Experiment
  Laser Ranging Retroreflector
  Apollo Lunar Surface Experiments Package (ALSEP) deployment:
    Each ALSEP experiment was connected by a cable to the ALSEP central station, which provided radio communication to Earth and electrical power from a radioisotope thermal generator.
    Passive Seismic Experiment
    Heat Flow Experiment
    Lunar Surface Magnetometer
    Cold Cathode Gauge (CCIG)
    Suprathermal Ion Detector Experiment (SIDE)
    Solar Wind Spectrometer
    Lunar Dust Detector
-In addition to their studies on the lunar surface, the Apollo 15 crew performed intensive studies of the Moon from lunar orbit. In addition to photography performed with hand-held cameras in the Command Module, a series of experiments were carried in the Scientific Instrument Module (SIM) on the Service Module. The same suite of SIM bay instruments was also flown on Apollo 16.
  Metric and Panoramic cameras
  Laser Altimeter
  S-Band Transponder Experiment
  X-ray Fluorescence Spectrometer Experiment
  Gamma-ray Spectrometer Experiment
  Alpha Particle Spectrometer Experiment
  Orbital Mass Spectrometer Experiment
  Bistatic Radar Experiment
  Apollo 15 Particles and Fields Subsatellite (PFS-1)
-In addition to their lunar studies, the Apollo 15 crew performed several experiments intended to explore various aspects of the space environment.
  Window Meteoroid Experiment
  Light Flashes Experiment
-More info: https://www.lpi.usra.edu/lunar/missions/apollo/apollo_15/experiments/ ; https://www.hq.nasa.gov/alsj/a15/a15mr-4.htm

## Slide 15: Apollo Lunar Surface Experiment Package
Lunar Sample Collection: Drill
Notes:       -Image credit: NASA  Dave Scott is using the rammer-jammer to probe the west Heat Flow hole. He has the Heat Flow sensor in his left hand and the vise/wrench in his right thigh pocket. In the drill-stem rack in the foreground, we can see the sections of the deep core that he has yet to drill. Image ID: AS15-92-12407.
      -Core tubes were used to obtain samples from below the Moon’s surface and were either pounded into the surface with a hammer or with the Apollo Lunar Surface Drill (Apollos 15-17).
      -The Apollo Lunar Surface Drill, used for the first time on Apollo 15, provided a means for one astronaut to emplace the Heat Flow Experiment probes below the lunar surface and collect a subsurface core. The performance of the drill was good. However, full depth penetration with the bore stems was a problem and extracting the core stems proved difficult (the cause of the problems was that it was assumed that the lunar soil was looser than it really was).
        The difficulty in the actual drilling activity was shown by Dave Scott’s hands, which would carry bruised fingernails from his efforts for several weeks after the mission.
        More info on the drilling problems: https://www.hq.nasa.gov/alsj/a15/a15carrier.html ; https://www.hq.nasa.gov/alsj/a15/a15.alsepdep.html
      -Two styles of core tubes were used on the Moon to obtain continuous soil columns down to 70 cm in depth.
        The initial style, used on Apollos 11, 12, & 14, was a thick-walled, small diameter (2 cm) tube called a core tube. This tube was designed to be easily opened in the laboratory; however, the soil column obtained in this type of tube was disturbed by the collection process.
        Therefore, a wider diameter (4 cm) tube with thinner walls was designed and fabricated for the last three missions (Apollos 15, 16, & 17). This tube was called a drive tube to distinguish it from the earlier core tube (both tubes took cores and both tubes were driven into the lunar regolith). A soil column collected in a drive tube was not significantly distorted by the coring process.
        -More info on Apollo lunar surface geological sampling tools: https://curator.jsc.nasa.gov/lunar/catalogs/other/jsc23454toolcatalog.pdf

## Slide 16: Surface Experiments on the Moon
On the Moon
Surface experiments
  Soil Mechanics Investigation
  Solar Wind Composition Experiment
  Laser Ranging Retroreflector
Notes: -Image credit: NASA  Dave Scott took this cross-Sun from the south of the Lunar Ranging Retroreflector (LRRR), showing the orientation gnomon and bubble level. Image ID: AS15-85-11468.
-In addition to their geologic studies, the Apollo 15 crew performed several experiments on the lunar surface.
  The Soil Mechanics Investigation studied the properties of the lunar soil.
  The Solar Wind Composition Experiment collected samples of the solar wind (electrically charged particles emitted by the Sun), allowing the chemical composition of the solar wind to be measured.
    The Solar Wind Composition Experiment was performed on Apollos 11, 12, 14, 15, and 16.
    On Apollo 15, the experiment was deployed roughly 15 m (50 ft) southwest of the lunar module at the end of the first EVA period and was retrieved at the end of the third EVA period, for a total foil exposure time of 41 hours and 8 min. Afterward, the aluminum foil was removed and returned to Earth for analysis.
  Laser Ranging Retroreflector (LRRR): Lasers fired from Earth are bounced back by the Laser Ranging Retroreflector to precisely measure the distance to the Moon.
    The Laser Ranging Retroreflector experiment was deployed on Apollos 11, 14, and 15 and has produced many important measurements, including an improved knowledge of the Moon’s orbit and the rate at which it is receding from Earth (currently 3.8 cm/yr) and of variations in the rotation of the Moon.
    The LRRR reflects laser pulses back to the telescopes on Earth used to illuminate it. By measuring the two-way travel time between the telescope and the LRRR, experiments can determine the distance between the two to a few centimeters.
    It consists of a series of corner-cube reflectors, which are a special type of mirror with the property of always reflecting an incoming light beam back in the direction it came from.
-More info: https://www.lpi.usra.edu/lunar/missions/apollo/apollo_15/experiments/; https://www.hq.nasa.gov/alsj/a15/a15mr-4.htm

## Slide 17: Apollo Lunar Surface Experiment Package
On the Moon
Apollo Lunar Surface Experiments Package (ALSEP)
  Passive Seismic Experiment
  Heat Flow Experiment
Notes:   -Image credit: NASA  This image shows the ALSEP Central Station, Solar Wind Spectrometer, Magnetometer, Heat Flow Electronics, SIDE/CCIG, and drill-stem rack. Image ID: AS15-92-12421.
  -The Apollo Lunar Surface Experiments Package (ALSEP) system consisted of a central station with a communications package and with leads running out to the instruments placed around it.
    Power was supplied by a radioisotope thermo-electric generator (RTG) – a plutonium fuel element was used.
    The power required by the whole station and experiments was less than the power of a 75-watt light bulb!
  -Apollo 15’s ALSEP consisted of 7 experiments: Passive Seismic Experiment, Heat Flow Experiment, Lunar Surface Magnetometer, Cold Cathode Gauge (CCIG), Suprathermal Ion Detector Experiment (SIDE), Solar Wind Spectrometer, & Lunar Dust Detector.
      Passive Seismic Experiment: detected lunar “moonquakes” and provided information about the internal structure of the Moon.
      Heat Flow Experiment: measured the amount of heat coming out of the Moon.
        The rate at which a planet loses its internal heat to space is an important control on the level of tectonism (faulting and folding of the planet’s surface due to internal deformation) and volcanic activity on the planet. This loss of internal heat was measured by the Heat Flow Experiment on Apollos 15 and 17. This experiment was also attempted on Apollo 16 but failed due to a broken cable connection.
  -More info on ALSEP: https://www.hq.nasa.gov/alsj/HamishALSEP.html

## Slide 18: Apollo Lunar Surface Experiment Package
On the Moon
Lunar Surface Magnetometer
Notes:   -Image credit: NASA  Close-up of the top of the Lunar Surface Magnetometer (LSM) from the northeast. The level bubble is visible at the center of the near surface. Image ID: AS15-86-11589.
      Lunar Surface Magnetometer: measured the strength of the Moon’s magnetic field.
        It was deployed to study intrinsic remanent magnetic fields and to observe the global magnetic response of the Moon to large-scale solar and terrestrial magnetic fields imposed on it.

## Slide 19: Apollo Lunar Surface Experiment Package
On the Moon
Cold Cathode Gauge Experiment
Suprathermal Ion Detector Experiment
Notes:   -Image credit: NASA  Down-Sun of the Suprathermal Ion Detector Experiment (SIDE) and the smaller Cold Cathode Gauge Experiment (CCIG). This experiment was also deployed on Apollos 12 and 14. The solid boom connecting the two packages is a new design feature. On the prior flights, the two packages were connected by a stiff cable which tended to retain loops and, whenever either package was moved, the other one would change orientation and/or tip over. The Apollo 15 SIDE/CCIG were deployed easily and without incident. Image ID: AS15-86-11595.
  -Two experiments, the Suprathermal Ion Detector Experiment (SIDE) and the Cold Cathode Gauge Experiment (CCIG) were used to measure the number and types of ions (an electrically charged molecule, either positive or negative) on the Moon. These ions are chiefly hydrogen and helium and are largely derived from the solar wind. The SIDE was used to measure the flux, number, density, velocity, and relative energy of the positive ions near the lunar surface.
    Cold Cathode Gauge Experiment: measured the abundance of gases in the tenuous lunar atmosphere at the lunar surface.
    Suprathermal Ion Detector Experiment (SIDE): studied the lunar ionosphere.

## Slide 20: Apollo Lunar Surface Experiment Package
On the Moon
Solar Wind Spectrometer
Lunar Dust Detector
Notes:   -Image credit: NASA  Cross-Sun from the south of the Solar Wind Spectrometer Experiment, from EVA-1. Image ID: AS15-86-11593.
      Solar Wind Spectrometer: measured the composition of the solar wind. An identical solar wind spectrometer was deployed on Apollo 12, which is 1100 km away on the Moon.
      Lunar Dust Detector: studied the effects of lunar dust on the operation of the experiment package.
        A lunar dust detector experiment was been deployed as a part of the ALSEP central station on Apollos 11, 12, 14, and 15. The experiment had 3 purposes:
          To measure the accumulation of dust from the LM ascent or from slow accretion processes
          To measure the lunar-surface brightness temperature from reflected infrared radiation
          To measure long-term high-energy-proton radiation damage.

## Slide 21: Lunar Roving Vehicle
Notes: -Image credits: NASA
  Right: Dave Scott took this photo as part of a panorama at the “VIP” parking site. It shows the rover at it’s final parking place. Image ID: AS15-88-11901
  Left: Jim Irwin took this photo of Dave maneuvering the rover at the start of the EVA-2 traverse. The Solar Wind Collector is visible beyond the rover TV camera.
    At the front of the rover, we can see the closed battery covers. In front of Jim’s seat, we can see his footrests.
    Note that there is dust coming off the wheels as Dave maneuvers.
    This picture also gives us a good view of Dave’s Remote Control Unit (RCU)-mounted Hasselblad camera and of the wire rover wheels.
    The traverse maps are mounted on Jim’s handhold and the Buddy Secondary Life Support System (BSLSS) bag is hanging from the back of Jim’s seat.
    Image ID: AS15-85-11471
-Apollo 15 saw the first flight of the Lunar Roving Vehicle (LRV). With the Lunar Roving Vehicle, total surface traverses increased from hundreds of meters during earlier missions to tens of kilometers during Apollos 15, 16 and 17. Astronauts were thus able to venture farther from the Lunar Module (LM).
-The TV antenna on the rover allowed people on Earth to monitor the astronauts’ exploration – they could feel like the third astronaut on the surface.
  At each stop on the surface, the astronauts would activate the camera and orient its antenna toward Earth. For the first time, scientists at Mission Control were able to look over the astronauts’ shoulders during surface exploration.
  Unlike the rover itself, the camera could be controlled from Earth by Ed Fendell’s Integrated Communications Officer (INCO) team, allowing scientists to direct the lunar activity, if necessary, based on what they could see.
-The empty weight of the rover was 462 lb (210 kg) on Earth and only 77 lb (35 kg) on the Moon, so the astronauts could use the U-shaped handles on the outer edges of the vehicle to lift and reposition the rover.
-The only problem the Apollo 15 crew experienced with the rover was the brief inoperability of the front steering mechanism. In spite of the problem, Scott and Irwin proceeded on their initial traverse using only the rear-wheel steering. The problem was fixed the following day prompting Scott to relay to Joe Allen, Apollo 15 mission scientist, at NASA’s Mission Control Center at Johnson Space Center, ”You know what I bet you did last night, Joe? You had some of those Marshall guys come up here and fix it didn’t you?” The LRV was developed, designed and built by NASA’s Marshall Space Flight Center.

## Slide 22: Driving on the Moon
Notes: -Video credit: NASA  Apollo 15 – 16-mm magazine 1246-EE ; https://history.nasa.gov/afj/ap15fj/a15videoindex.html
  View from the moving lunar roving vehicle, following its own outbound tracks. Mount Hadley, a 15,000-foot mountain at the north end of the embayment, is in the distance at right.
  All shot at 24 frames per second.

## Slide 23: Apollo 12 Traverses
Notes: -Image source: https://www.lpi.usra.edu/publications/slidesets/apollolanding/ApolloLanding/slide_25.html
-The Apollo 15 traverses.
-The thick lines indicate the paths taken by the astronauts during the three EVAs. Numbered spots indicate sampling stations along the individual traverses.
  During the first EVA (beginning at 9:13 a.m. EDT on July 31): the crew conducted a 10.3-kilometer geological traverse and deployed some lunar surface experiments. Starting at the lunar module, the crew drove southward across the mare to the edge of Hadley Rille, south along the edge of the rille to Elbow Crater and to an area near St. George Crater. The return route was past Elbow Crater and directly across the mare to the lunar module. After returning to the LM, the astronauts unloaded and deployed the Apollo Lunar Surface Experiments Package (ALSEP). The EVA lasted approximately 6 hours, 33 minutes, ending at 3:46 p.m.
  During the second EVA (beginning at 7:49 a.m. EDT on August 1): the crew conducted a 12.5-kilometer traverse southeast across the mare and near Index, Arbeit, Crescent, Dune, and Spur craters along the base of the Apennine Mountains. The return traverse closely followed the outbound route. After unloading the samples, the astronauts made a second trip to the ALSEP site to perform some additional tasks. The duration of the second EVA was approximately 7 hours, 12 minutes, ending at 3:01 p.m.
  During the third EVA (beginning at 4:52 a.m. EDT on August 2, about 1.5 hours late to allow the crew to get some additional rest): the crew conducted a 5.1-kilometer traverse west to Scarp Crater and northwest along the edge of Hadley Rille, and east across the mare to the lunar module. The EVA was shortened to approximately 4 hours and 50 minutes to meet the liftoff timeline.
-The diagram is based on the Apollo 15 Traverses Lunar Photomap Edition 2, Sheet 41B4S4[25].
-More traverse images: http://lroc.sese.asu.edu/posts/491

## Slide 24: Apollo 12 Traverses
Thomas Schwagmeier and Eric M. Jones
Notes: -Image credit: Thomas Schwagmeier and Eric M. Jones
-Overlay of the Apollo 15 traverse map on Manhattan, New York City.
-Because of the Lunar Roving Vehicle, the Apollo 15 crew was able to travel much farther from the lunar module than any of the previous Apollo missions.
-Source: https://www.hq.nasa.gov/alsj/TraverseMapsEarth.html

## Slide 25: Apollo 12 landing site, as imaged by the Lunar Reconnaissance Orbiter Camera
NASA/GSFC/Arizona State University
Notes: -Image credit: NASA/GSFC/Arizona State University  http://www.lroc.asu.edu/posts/783
-Traverse plots of the first two Apollo 15 EVAs, on which astronauts Scott and Irwin ventured to the lower slopes of Mons Hadley Delta (center left); numbers indicate elevations above the landing site (LM).
-For scale, the distance the astronauts travelled from the LM to Elbow crater along the edge of Hadley Rille (EVA 1) is ~4.5 km.

## Slide 26: Apollo 12 landing site, as imaged by the Lunar Reconnaissance Orbiter Camera
Notes: -Image credit: LROC  http://lroc.sese.asu.edu/featured_sites/view_site/4
-A zoomed in version of the Apollo 15 landing site, as imaged by the Lunar Reconnaissance Orbiter Camera (taken on March 2, 2010). Note that this zoomed in version doesn’t show all of the EVA traverses, which had a maximum range of about 3 miles from the LM.

## Slide 27: Hadley Rille
Notes: -Image credit: NASA  This frame from Jim Irwin’s EVA-3 Station 9a pan shows the bend of Hadley Rille near Elbow Crater. Image ID: AS15-82-11122.
-The third EVA began at 4:52 a.m. EDT on August 2, about 1.5 hours late to allow the crew to get some additional rest. This EVA included a 5.1-kilometer traverse west to Scarp Crater and northwest along the edge of Hadley Rille, and east across the mare to the lunar module. The EVA was shortened to approximately 4 hours and 50 minutes to meet the liftoff timeline.
-Commentary from the Apollo Lunar Surface Journal: https://www.hq.nasa.gov/alsj/a15/a15.rille.html

## Slide 28: Apollo Lunar Surface Experiment Package
Moon Mail
Notes:       -Image credits: NASA  Source: https://history.nasa.gov/alsj/a15/a15PostalKit.html
        Right: Post-flight photo of the Postal Kit with a mission patch added. The cancellation device in the left foreground is a duplicate of the flown item which is believed to have been left on the Moon.
        Left: Photo of the First Day Cover cancelled on the Moon by Dave Scott during the EVA-3 close-out on August 2, 1971. It carries two advanced, hand-perforated die proofs of stamps celebrating the U.S. space program. Smudges at bottom left are “thumbprints” Scott made with Moon dust using his space-suit glove.
        -Commentary from the Apollo 15 Lunar Surface Journal:
            167:18:43 Scott: Okay. To show that our good Postal Service has deliveries any place in the universe, I have the pleasant task of canceling, here on the Moon, the first stamp of a new issue dedicated to commemorate United States achievements in space. And I’m sure a lot of people have seen pictures of the stamp. I have the first one here on an envelope. At the bottom it says, “United States in space, a decade of achievement,” and I’m very proud to have the opportunity here to play postman. I pull out a cancellation device. Cancel this stamp. It says, “August the second, 1971, first day of issue”.
            [Dave gets a rubber stamp out of the cloth Post Office kit and presses it on what looks like an ink pad.]
            167:19:30 Scott: What could be a better place to cancel this stamp than right here at Hadley Rille. (Pause)
            [Dave places the envelope on a flat surface on the Modularized Equipment Stowage Assembly (MESA) and, after carefully positioning the rubber stamp, presses it down and then lifts it off.]
            167:19:48 Scott: By golly, it even works in a vacuum. (Pause)
            [Dave examines the envelope.]
            167:19:51 Scott: But not too well. But it’s the first time, so I guess they’re just learning. (Pause)
            [Dave re-cancels the envelope.]
            167:20:11 Irwin: You can put a thumbprint on there, Dave.
            167:20:14 Scott: Well...
            167:20:15 Irwin: If there’s room left.
            167:20:17 Scott: I’ve got several dusty thumbprints. Now, I’ll stick this back in our special mail pouch here, and we’ll deliver it when we return.
            [The Post Office bag and the First Day Cover are on display at the Smithsonian Institution’s National Postal Museum in Washington, D.C.]
      -During the EVA-3 close-out, Dave Scott made history when he became the first person to cancel a stamp on an interplanetary envelope.
      -More info: https://history.nasa.gov/alsj/a15/a15PostalKit.html ; https://postalmuseum.si.edu/exhibition/stamps-take-flight-rarities-and-special-holdings/moon-mail

## Slide 29: Apollo Lunar Surface Experiment Package
Confirming Galileo’s law of free fall
A Feather & a Hammer
Notes:       -Video credit: NASA  Source: https://www.hq.nasa.gov/alsj/a15/a15.clsout3.html
        Commentary:
          167:22:06 (mission elapsed time) Dave Scott: Well, in my left hand, I have a feather; in my right hand, a hammer. And I guess one of the reasons we got here today was because of a gentleman named Galileo, a long time ago, who made a rather significant discovery about falling objects in gravity fields. And we thought where would be a better place to confirm his findings than on the Moon.
          167:22:28 Scott: And so we thought we’d try it here for you. The feather happens to be, appropriately, a falcon feather for our Falcon. And I’ll drop the two of them here and, hopefully, they’ll hit the ground at the same time. (Pause)
          [Dave is holding the feather and hammer between the thumb and forefinger of his left and right hands, respectively, and has his elbows up and out the side. He releases the hammer and feather simultaneously and pulls his hands out of the way. The hammer and feather fall side by side and hit the ground at virtually the same time.]
          167:22:43 Scott: How about that!
          167:22:45 Joe Allen: How about that! (Applause in Houston)
          167:22:46 Scott: Which proves that Mr. Galileo was correct in his findings. (Pause)
          167:22:58 Allen: Superb.
      -During EVA-3, Dave Scott demonstrated Galileo’s discovery about falling objects in gravity fields. In his left hand, he held onto a falcon feather while in his right, he held a hammer. He then dropped them both at the same time, and they both hit the ground simultaneously (since there’s no atmosphere on the Moon, they fell side by side. They did fall more slowly than on Earth though because the gravity is 1/6 that of Earth’s), thus confirming Galileo’s law of motion concerning falling bodies.
        After more than 3 ½ centuries, at a distance of 239,000 miles give or take a few, from his home in Florence, Italy, Galileo Galilei’s discovery that “gravity pulls all bodies equally regardless of their weight” was clearly and vividly demonstrated before a television audience that spanned the planet Earth.

## Slide 30: Apollo Lunar Surface Experiment Package
A Feather & a Hammer
Alan Bean
Notes:       -Image credit: Alan Bean (Apollo 12 astronaut)  http://alanbeangallery.com/hammerfeather-story.html
        A painting depicting the Apollo 15 feather/hammer demo, created by Apollo 12 astronaut and artist, Alan Bean.
        Painting Completed 1986
        48 x 37 1/2 inches, Acrylic on Masonite

## Slide 31: Surface Experiments on the Moon
A Lunar Memorial
Notes: -Image credit: NASA  Image ID: AS15-88-11894 ; Dave Scott created a small memorial at the final Lunar Roving Vehicle parking place to honor the astronauts and cosmonauts who had died prior to Apollo 15. Their names are inscribed in alphabetical order on the plaque. The figurine, Fallen Astronaut, was created by Belgian artist Paul van Hoeydonck.

## Slide 32: Surface Experiments on the Moon
Metric and Panoramic Cameras
Laser Altimeter
S-Band Transponder Experiment
X-ray Fluorescence Spectrometer Experiment
Science Experiments in Orbit (1)
Notes: -Image credit: NASA  Apollo 15 Scientific Instrument Module (SIM) bay viewed from the LM during Rev 49, after rendezvous. Image ID: AS15-88-11973.
-In addition to their studies on the lunar surface, the Apollo 15 crew performed intensive studies of the Moon from lunar orbit. In addition to photography performed with hand-held cameras in the Command Module, a series of experiments were carried in the Scientific Instrument Module, or SIM (the first to fly and operate on an Apollo spacecraft), on the Service Module. The same suite of SIM bay instruments was also flown on Apollo 16.
  The Metric and Panoramic Cameras provided systematic photography of the lunar surface.
  The Laser Altimeter measured the heights of lunar surface features.
  The S-Band Transponder Experiment measured regional variations in the Moon’s gravitational acceleration.
  The X-ray Fluorescence Spectrometer Experiment measured the composition of the lunar surface.
-More info: https://www.lpi.usra.edu/lunar/missions/apollo/apollo_15/experiments/

## Slide 33: Surface Experiments on the Moon
Gamma-ray Spectrometer Experiment
Alpha Particle Spectrometer Experiment
Orbital Mass Spectrometer Experiment
Bistatic Radar Experiment
Science Experiments in Orbit (2)
Notes: -Image credit: NASA  Apollo 15 Scientific Instrument Module (SIM) bay viewed from the LM during Rev 49, after rendezvous. Image ID: AS15-88-11973.
-In addition to their studies on the lunar surface, the Apollo 15 crew performed intensive studies of the Moon from lunar orbit. In addition to photography performed with hand-held cameras in the Command Module, a series of experiments were carried in the Scientific Instrument Module, or SIM (the first to fly and operate on an Apollo spacecraft), on the Service Module. The same suite of SIM bay instruments was also flown on Apollo 16.
  The Gamma-ray Spectrometer Experiment measured the composition of the lunar surface.
  The Alpha Particle Spectrometer Experiment measured radon emission from the lunar surface.
  The Orbital Mass Spectrometer Experiment measured the composition of the lunar atmosphere.
  The Bistatic Radar Experiment measured the scattering of radar waves from the lunar surface.
  The Apollo 15 Particles and Fields Subsatellite (PFS-1) measured regional variations in the Moon’s gravitational acceleration and magnetic field and the distribution of charged particles around the Moon.
-In addition to their lunar studies, the Apollo 15 crew performed several experiments intended to explore various aspects of the space environment.
  The Window Meteoroid experiment studied impacts on the windows of the Apollo 15 Command Module to obtain information about the size distribution of very small micrometeorites.
  The Light Flashes Experiment studied light flashes seen by the crew that are related to charged particles in space.
-More info: https://www.lpi.usra.edu/lunar/missions/apollo/apollo_15/experiments/

## Slide 34: Surface Experiments on the Moon
Launching a Subsatellite
Notes: -Image credits: NASA
  Left: The Apollo 15 Particles and Fields Subsatellite (PFS-1) was a small satellite released into lunar orbit from the Apollo 15 Service Module.  https://nssdc.gsfc.nasa.gov/image/spacecraft/apollo_subsat.jpg
  Right: The launch of the PFS-1.  https://history.nasa.gov/afj/ap15fj/photos/q/subsat.jpg
-On August 4, 1971, the Apollo 15 crew prepared to come home. On the last orbit around the Moon, they placed a subsatellite in orbit around the Moon, the first-ever launched by a crewed spacecraft.
  The PFS-1 measured regional variations in the Moon’s gravitational acceleration and magnetic field and the distribution of charged particles around the Moon.
-The Moon’s roughly circular orbit about the Earth at ~380,000 km (60 Earth radii) carried the subsatellite into both interplanetary space and various regions of the Earth’s magnetosphere. The satellite orbited the Moon and returned data from August 4, 1971 until January 1973. It is assumed the subsatellite’s orbit decayed, and it impacted the Moon sometime after this; the impact site is unknown.
-A virtually identical subsatellite was also deployed by Apollo 16.
-More info: https://nssdc.gsfc.nasa.gov/nmc/spacecraft/display.action?id=1971-063D

## Slide 35: Spacewalk: A Long Way from Home
Notes: -Image credits: NASA
  Right: Apollo 15 trans-Earth EVA view ; Image ID: S71-43202.
    Astronaut Al Worden, command module pilot of Apollo 15, floats in space outside the spacecraft during his trans-Earth extravehicular activity (EVA). This photograph was taken from a frame of motion picture film exposed by the 16mm Maurer camera mounted in the hatch of the Command Module (CM).
    During his EVA, Worden inspected the Service Module’s (SM) Scientific Instrument Module (SIM) bay and retrieved the film cassettes from the Panoramic Camera and the Metric Camera.
      The SIM bay held 8 orbital science experiments.
    The EVA occurred when the spacecraft was homeward bound approximately 171,000 nautical miles (197,000 miles) from Earth.
  Left: NASA drawing depicting the EVA. https://www.hq.nasa.gov/alsj/a15/ap15-S71-39614HR.jpg
-On Aug. 5, 1971, Al Worden became the first human to carry out a deep space EVA. He exited the CM, climbed toward the rear of the SM and retrieved the 8,000 ft of film contained in the casettes from the SIM bay cameras and returned to the CM.
  The entire operation was completed in 39 minutes (one hour had been scheduled in the flight plan).
-Associated commentary and video: https://history.nasa.gov/afj/ap15fj/23b-day11_worden_eva.html

## Slide 36: Splashdown
Splashdown
Notes: -Image credits: NASA
  Left image: Apollo 15 descends toward splashdown with one fouled chute. Image ID: S71-41999.
  Top right image: Apollo 15 splashdown. Image ID: S71-43543.
  Bottom right image: The Apollo 15 astronauts were in good spirits after leaving their spacecraft and awaiting helicopter pickup from a life raft during recovery operations at the completion of their 12-day lunar mission. From left-to-right: Mission Commander David R. Scott, James B. Irwin, and Alfred M. Worden. They were welcomed aboard the USS Okinawa approximately 40 minutes after splashdown. Image ID: 71-H-1237.
-The Apollo 15 splashdown occurred at 4:46 p.m. EST on August 7, 1971 in the Pacific Ocean, about 335 mi (539 km) north of Honolulu, Hawaii.
  The crew was picked up by helicopters from the prime recovery ship, the USS Okinawa, 6.32 mi (10.2 km) from the targeted touchdown point.
-During the command module’s final stages of descent, one of its 3 parachutes became only partially inflated. However, the landing system was designed to use just 2 parachutes; the third was an added safety factor. As a result of the loss of one parachute, the command module impacted at 21.8 mph, instead of the planned 19 mph.

## Slide 37: Returned Samples
Returned Samples
Notes: -Image credits: NASA/JSC
  Left: Dave Scott and Joe Allen (EVA CapCom/mission scientist) examine sample 15415 in the Lunar Receiving Lab after the flight. Image ID: S71-43477.
  Right: Apollo 15 basalt 15555 has a mass of 9.6 kilograms and is one of the largest individual lunar samples collected during the Apollo program. Image ID: S71-43954.
  -The overall set of lunar samples collected during the Apollo program can be classified into three major rock types: basalts, breccias, and lunar highland rocks. Apollo 15 collected important examples of all three rock types.
  -Apollo 15 landed in Mare Imbrium at the base of the Apennine Mountains, which forms part of the rim of the Imbrium impact basin. There were two main geology objectives for this site: to collect rocks from the Apennine mountains and to study Hadley Rille, a volcanic channel near the landing site.
  -The Apollo 15 crew collected 370 individual rock and soil samples, including a deep drill core with material from 2.4 meters below the lunar surface, with a total mass of 77 kilograms.
    The surface rocks in Mare Imbrium are basalt which are dark-colored rocks that solidified from molten lava. They are rich in iron and consist primarily of the minerals pyroxene and plagioclase with some olivine.
    Another type of volcanic material found at the Apollo 15 landing site is pyroclastic glass. Several types of volcanic glass occur in the Apollo 15 samples, the most common and famous of which is the green glass. This glass is very rich in the element magnesium, which causes the green color.
  -Apollo 15 sample catalog: https://www.hq.nasa.gov/alsj/a15/a15sampcat.html
  -More about the returned samples: https://www.lpi.usra.edu/lunar/missions/apollo/apollo_15/samples/
  -JSC Lunar Sample Compendium: https://curator.jsc.nasa.gov/lunar/lsc/index.cfm

## Slide 38: Returned Samples
Genesis Rock
Notes: -Image credit: NASA/JSC  NASA Johnson’s Lunar Receiving Lab photo of sample 15415, a 269 gram piece of pure anorthosite – dubbed the “Genesis Rock” by the press – that Dave and Jim collected at Spur Crater during EVA-2. The black cube next to the sample is one inch on a side. Image ID: S71-42955.
-On Aug. 1, 1971, during the second EVA, at the Station 7 site at Spur Crater, the crew gathered selected samples and a comprehensive soil sample. In all, 93 samples were collected, including the sample that became known as the “Genesis Rock.”
  At Spur Crater on Mount Hadley Delta, the astronauts collected an anorthosite, a rock that is composed almost entirely of the mineral plagioclase. This rock is now known as “Genesis Rock” because it provided important information in helping to unravel the formative processes of the Moon, Earth, and planets.
  Early in the Moon’s history, there was a stage known as the magma ocean in which the Moon’s outer layers were molten. As the magma ocean cooled and solidified, the plagioclase-rich anorthosite floated on the surface like icebergs in the Earth’s oceans. The existence of the magma ocean phase was first recognized from small fragments in the Apollo 11 samples, but Apollo 15’s Genesis Rock is important because it is much larger than any previous sample of lunar anorthosite. Apollo 16 later collected anorthosite samples that are both larger and older than Genesis Rock.
  Studies of Genesis Rock indicate an age of about 4.1 billion years. However, it is believed that this represents a time when the rock experienced a metamorphic alteration and that the rock is actually older than 4.1 billion years.
  Norite and anorthositic norite samples, also collected at Spur Crater, are composed primarily of plagioclase and pyroxene and are about 4.5 billion years old, virtually as old as the Moon itself. They likely formed in the deeper part of the magma ocean and were brought to the lunar surface by the Imbrium basin-forming impact.
-Commentary from sample collection on the Moon: https://www.hq.nasa.gov/alsj/a15/a15.spur.html

## Slide 39: By the Numbers
18 hrs, 37 min spent outside the lander
17.3 mi (28 km) total length of EVA drive traverses
170 lbs (77 kg) of samples collected
295 hrs (~12 days) total mission time
By the Numbers
Notes: -Image credit: NASA  EVA-1 Closeout – Jim Irwin is at the back of the Rover, and St. George and Hadley C are in the distance.  https://www.hq.nasa.gov/alsj/a15/a15.1254512_dmh.jpg
-Farthest point traveled from the LM: ~3 mi (~5 km)
-Improved technology enabled a longer stay on the Moon (nearly 3 days)!
-Compare to Apollo 11:
  60 m – farthest point traveled from the LM
  2.5 hrs spent outside the lunar module
  47.8 lbs of samples collected
  195 hrs, 18 min, 35 sec (~8 days) total mission time

## Slide 40: Apollo 15 Command Module
Name: “Endeavour”
Location:
  National Museum of the United States Air Force
  Wright-Patterson Air Force Base, Dayton, OH
Notes: -Image credit: National Air and Space Museum  https://airandspace.si.edu/collection-objects/command-module-apollo-15
-Color of the command module is due to the mylar material used.

## Slide 41: More Info
More Info
Notes: -Image credit: NASA  Jim Irwin’s view from EVA-1’s Elbow Crater, Station 1. The crater is a bit washed out in this down-Sun photo. Beyond the crater, we can see the west-trending portion of the rille that skirts the base of the mountain and then turns south again. Image ID: AS15-85-11398.

## Slide 42: Apollo Landing Sites
Apollo Landing Sites
Notes: -Image credit: NASA/GSFC/Arizona State University
-Left: Apollo landing sites (lunar near side)
-Right: Lunar far side
(captured by the Lunar Reconnaissance Orbiter spacecraft)

## Slide 43: Apollo 11 Traverses
Apollo 11 Traverses  New York City
Notes: -Image credit: NASA/GSFC/Brent Garry
-Apollo 11 tracks overlain on the Intrepid Sea, Air & Space Museum in New York City, NY.
-Future Apollo missions would travel up to ~5 mi from the lunar module (Apollo 17).

## Slide 44: Apollo 12 Traverses
Apollo 12 Traverses  Rome
Notes: -Image credit: Thomas Schwagmeier
-The Apollo 12 traverse map superimposed on a simplified map of Rome.
-Note that Surveyor Crater is slightly larger than the Coliseum.
-Source: https://www.hq.nasa.gov/alsj/TraverseMapsEarth.html

## Slide 45: Apollo 12 Traverses
Apollo 14 Traverses  Washington, D.C.
Notes: -Image credit: Thomas Schwagmeier
-Overlay of the Apollo 14 traverse map, derived from high-resolution Lunar Reconnaissance Orbiter Camera images, on a simplified map of Washington D.C.
-With the lunar module placed at the Lincoln Memorial, the center of Cone crater is on E Street between the South Lawn of the White House and the Ellipse.
-Source: https://www.hq.nasa.gov/alsj/TraverseMapsEarth.html

## Slide 46: Apollo 12 Traverses
Apollo 16 Traverses  Sydney
Notes: -Image credit: Thomas Schwagmeier
-The Apollo 16 traverse map superimposed on a simplified map of Sydney.
-Source: https://www.hq.nasa.gov/alsj/TraverseMapsEarth.html

## Slide 47: Apollo 17 Traverses
Apollo 17 Traverses  New York City
Notes: -Image credit: NASA/GSFC/Brent Garry
-Apollo 17 tracks overlain on New York City, NY.

## Slide 48: JFK’s Speech
The Decision to Go to the Moon
  May 25, 1961
We Choose to Go to the Moon
  September 12, 1962
JFK’s Speech
Notes: -Image source: https://history.nasa.gov/moondec.html  JFK’s address to Congress.
-”The Decision to Go to the Moon”: President John F. Kennedy's May 25, 1961 Speech before Congress. JFK announced before a special joint session of Congress the dramatic and ambitious goal of sending an American safely to the Moon before the end of the decade.
-”We choose to go to the Moon” is the famous tagline of a speech about the effort to reach the Moon delivered by President John F. Kennedy to a large crowd gathered at Rice Stadium in Houston, Texas on September 12, 1962.

## Slide 49: Additional Resources
Apollo Images:
  https://images.nasa.gov/
  https://history.nasa.gov/alsj/a15/images15.html
  http://lroc.sese.asu.edu/featured_sites#ApolloLandingSites
Apollo Videos:
  https://svs.gsfc.nasa.gov/Gallery/apollo.html
Apollo 15 General:
  https://nssdc.gsfc.nasa.gov/planetary/lunar/apollo15info.html
  https://www.lpi.usra.edu/lunar/missions/apollo/apollo_15/overview/
  Preliminary Science Report: https://www.hq.nasa.gov/alsj/a15/as15psr.pdf
Additional Resources