## Slide 1: Apollo 17
Presenter’s name
Presenter’s title/position
NASA/GSFC/Arizona State University
Notes: -Image credit: NASA/GSFC/Arizona State University  An oblique image of the Taurus-Littrow valley (Apollo 17 landing site) taken by the Lunar Reconnaissance Orbiter Camera (LROC) on March 29, 2015.
-For mission patch image, see https://history.nasa.gov/apollo_patches.html
-Note: This presentation provides a brief overview of the Apollo 17 mission to the Moon and thus does not include everything; however, links to support further research are included at the end.
-Tips:
  You do not need to use everything in this presentation!
  Feel free to alter/edit this presentation to fit your specific needs/audience
-Updated December 2022

## Slide 2: NASA Press Releases
Notes: -NASA press releases (Dec. 1972): https://historydms.hq.nasa.gov/sites/default/files/DMS/e000013883.pdf

## Slide 3: NASA Press Releases
Notes: -NASA press releases (Dec. 1972): https://historydms.hq.nasa.gov/sites/default/files/DMS/e000013883.pdf

## Slide 4: Overview
December 7-19, 1972
Eugene A. Cernan
  Commander
Ronald E. Evans
  Command module pilot
Dr. Harrison H. “Jack” Schmitt
  Lunar module pilot
Notes: -Image credit: NASA  With the Apollo 17 Saturn V launch vehicle in the background, the crew is photographed with a lunar roving vehicle trainer. Eugene Cernan (commander) is seated with Jack Schmitt (lunar module pilot), standing on the left, next to Ronald Evans (command module pilot).
-Sixth and final human Moon landing: Cernan and Schmitt landed on the lunar surface on December 11, 1972, at 2:55pm ET, with the first extravehicular activity beginning four hours later.
-Apollo 17 was the final in a series of three J-type missions planned for the Apollo program. These J-type missions can be distinguished from previous G- and H-series missions by extended hardware capability, larger scientific payload capacity and by the use of the battery-powered Lunar Roving Vehicle, or LRV.
-The mission plan for Apollo 17 had several scientific objectives for the crew to accomplish: geological surveying and sampling of materials and surface features in a pre-selected area of the Taurus-Littrow region; deploying and activating surface experiments; and conducting in-flight experiments and photographic tasks during lunar orbit and the return journey back to Earth.
-Eugene Cernan was the mission commander and was the pilot of Gemini 9 and the lunar module pilot of Apollo 10. Cernan was the twelfth and final person to land on the Moon during Apollo.
-Ronald Evans was the command module pilot and was a member of the astronaut support crews for Apollo 7 and Apollo 11 as well as the backup command module pilot for Apollo 14.
-Dr. Harrison H. “Jack” Schmitt was the lunar module pilot and was the first scientist to go to the Moon. Schmitt was designated as the mission scientist in support of Apollo 11 and was the backup lunar module pilot for Apollo 15.

## Slide 5: Surface Experiments on the Moon
Field Training on Earth
Notes: -Image credits: NASA
  Left: Apollo 17 astronaut Jack Schmitt stands at the rim of a crater during geology training in Flagstaff, Arizona.
  Right: Jack Schmitt (left), and Eugene Cernan (right) ride the Grover, the ground-based training version of the Lunar Roving Vehicle.
-To prepare for their exploration of the Moon and to gain firsthand experience with a diversity of geologic formations, the Apollo 17 astronauts underwent a variety of field training.
  As with Apollos 15 and 16, Apollo 17’s mission focused primarily on lunar geology. In addition to receiving many hours of classroom lectures on the subject, the Apollo 17 astronauts participated in several geology field trips to sites similar to the terrain expected at the Taurus-Littrow landing site on the Moon.
  In May 1972, the astronauts, accompanied by a team of geologists, traveled to Sudbury, Ontario, Canada, the site of a meteorite impact. Following an aerial survey of the area, Cernan and Schmitt spent two days inspecting the local geology.
  In June 1972, the crew spent a week in Hawaii, using the Grover, a terrestrial version of the Lunar Roving Vehicle (LRV) designed by the U.S. Geological Survey, on several traverses across the lava flows of the Kilauea and Mauna Kea volcanos.
  In July 1972, the crew spent two days exploring igneous formations in Stillwater, Montana, and in August 1972, another two days exploring artificial craters created by underground nuclear explosions at the Nevada Test Site near Tonopah, Nevada.
  On Sept. 6-7, 1972, Eugene Cernan and Jack Schmitt, along with their backups John Young and Charlie Duke, and a team of geologists, traveled to Tonopah, Nevada.
    Over the course of two lunar traverse simulations, the astronauts used the Grover to explore Lunar Crater, a relatively young, little-eroded volcanic feature that shared characteristics with the Apollo 17 landing site landscape.
  On Nov. 2-3, 1972, Eugene Cernan and Jack Schmitt, along with their backups John Young and Charlie Duke, participated in the final geology training field trip of the Apollo program. In this field exercise, the astronauts, assisted by a team of geologists, conducted two simulated lunar traverses, one at Sunset Crater and the other at Cinder Lake in the San Francisco volcanic field near Flagstaff, Arizona.
    During the exercises, they communicated with the science support room in Mission Control at the Manned Spacecraft Center (MSC), now NASA’s Johnson Space Center in Houston, staffed by the same teams who supported them during the actual mission.
    The astronauts incorporated several of the lunar surface science experiments into the training session and practiced driving the Grover.
-More info: https://www.nasa.gov/feature/50-years-ago-six-months-until-apollo-17 ; https://www.nasa.gov/feature/50-years-ago-three-months-until-apollo-17 ; https://www.nasa.gov/feature/50-years-ago-flight-readiness-review-clears-apollo-17-for-launch

## Slide 6: Launch
Launch
Notes: -Image credit: NASA  Apollo 17 liftoff.
-Apollo 17 was the first night launch of the Saturn V rocket.
-The 363-foot-tall Apollo 17 space vehicle launched from Pad A, Launch Complex 39, Kennedy Space Center, at 12:33 a.m. EST on Dec. 7, 1972.
  A technical problem caused a 2 hour 40-minute delay in the launch.
-More about the launch: https://history.nasa.gov/afj/ap17fj/01_day01_launch.html

## Slide 7: Saturn V Size Comparison
Notes: -Image credit: NASA  1967 illustration compares the Apollo Saturn V spacecraft (363 ft) of the Moon Landing era to the Statue of Liberty (305 ft).
-A Saturn V rocket has 3 stages, 11 powerful rocket engines, and huge tanks for kerosene (RP-1) and liquid hydrogen and oxygen. It’s still the largest crewed rocket ever flown and the only one to carry humans beyond Earth orbit.
  Height: 111 meters (363 feet)
  Diameter: 10 meters (33 feet)
  Mass: 2,840,622 kg (6,262,500 pounds) at liftoff (about 100 fully loaded tractor-trailers – only 1% of this actually goes to the Moon)
  Maiden Flight: Nov. 9, 1967 (uncrewed)
  The rocket generated 34.5 million newtons (7.6 million pounds) of thrust at launch, creating more power than 85 Hoover Dams.
  Could launch about 43,500 kg (50 tons) to the Moon (about the same as 4 school buses).
  The Apollo 17 launch vehicle was the twelfth in the Apollo Saturn V series and was the tenth crewed Saturn V vehicle.
  More info on Saturn V: https://solarsystem.nasa.gov/news/337/what-was-the-saturn-v/

## Slide 8: Apollo Spacecraft Design
Apollo Spacecraft
Engine Bell
Thrusters
High-Gain Antenna
Thrusters
Thrusters
Descent Stage
Ascent Stage
Command Module
Service Module
Challenger Lunar Module
America Command Module
Notes: -Image credit: NASA  Diagram of the combined Apollo command and service module/lunar module translunar coast configuration.
-The lunar module was named Challenger while the command module was named America for Apollo 17.
-Source: https://history.nasa.gov/afj/ap13fj/04day1-end.html

## Slide 9: Surface Experiments on the Moon
Moon Bound
Notes: -Image credits: NASA  Views of Earth during translunar coast (outbound journey to the Moon), with Earth growing steadily smaller as the Apollo 17 astronauts ventured farther and farther away.
-More: http://tothemoon.ser.asu.edu/gallery/Apollo/17/Hasselblad%20500EL%2070%20mm#AS17-148-22727

## Slide 10: Apollo 12 Landing Site
Moon on December 11, 1972
Apollo 17 Landing Site
Notes: -Image credit: NASA's Scientific Visualization Studio  https://svs.gsfc.nasa.gov/4302
  Visualization of the Moon as viewed from Earth at the time of the Apollo 17 Moon landing on December 11, 1972.
-The Apollo 17 landing occurred in the Taurus-Littrow valley region of the Moon.

## Slide 11: Overview
Taurus-Littrow Valley
NASA/GSFC/Arizona State University
Notes: -Image credit: NASA/GSFC/Arizona State University  An oblique image of the Taurus-Littrow valley taken by the Lunar Reconnaissance Orbiter narrow-angle camera. The Apollo 17 lunar module descent stage shadow is precisely centered in the image (denoted by the arrow). The resolution is about 4 meters per pixel.  https://svs.gsfc.nasa.gov/4302
-The Apollo 17 landing site in Taurus-Littrow valley is a relatively flat spot among low mountains at the southeastern edge of Mare Serenitatis. The landing zone is named after the Taurus Mountains and the Littrow Crater to its north.
-The Taurus-Littrow site’s mix of mountain rockslides and volcanic cinder cones, yielding older and younger samples, respectively, would help fill the gaps in scientists’ understanding of the Moon’s history.
  There were two main geology objectives for this site: to obtain samples of ancient rocks from the lunar highlands crust and to look for evidence of young volcanic activity on the valley floor.
-More info: https://www.nasa.gov/feature/50-years-ago-nasa-selects-landing-site-for-apollo-17

## Slide 12: Pete Conrad stepping on the lunar surface
“Okay, Houston. The Challenger has landed!”
Notes: -Image credits: NASA
  Left: A pre-extravehicular activity (EVA)-1 lunar module window pan. South Massif and Geophone Rock are in view. Image ID: AS17-147-22488.
  Right: A pre-extravehicular activity (EVA)-1 lunar module window pan. North Massif and a Reaction Control System (RCS) thruster are in view. Image ID: AS17-147-22472.
  -Transcript between astronauts and Houston Mission Control (times are elapsed time after launch):
  113:02:11 Cernan: Okay, Houston. The Challenger has landed!
  113:02:15 Fullerton: Roger, Challenger. That’s super.
  113:02:17 Schmitt: Okay, Parker valves...
  [Schmitt - "Parker valves (also known as the isolation valves or shut-off valves) controlled the RCS thrusters - the fuel and oxidizer - and there was always some concern that they might close at landing, just because of the little bit of shock. So the procedure was to go through and cycle (close and open) every one of them. There were, I don't know, sixteen of them on the wall in front of me and, while Gene was getting all excited, I was cycling switches."]
  113:02:23 Cernan: (Responding to Fullerton) Boy, you bet it is, Gordo. (To Jack) Boy, when you said shut down, I shut down and we dropped, didn’t we?
  113:02:28 Schmitt: Yes, sir! But we is here.
  113:02:30 Cernan: Man, is we here.
  -Source: Eric M. Jones; https://www.hq.nasa.gov/alsj/a17/a17.landing.html
  -Apollo 17 in Real Time: https://apolloinrealtime.org/17/?t=113:02:13

## Slide 13: Pete Conrad coming down the ladder from the lunar module
Lunar geology studies
Lunar sample collection
Lunar surface science experiments
Orbital science experiments
  Lunar-focused
  Space environment-focused
Science-focused Mission
Notes:       -Image credit: NASA  Jack Schmitt’s first color photo taken at the Apollo Lunar Surface Experiments Package (ALSEP) site. He has just deployed Geophone 4, the last of the set of four. Visible in the image are Geophone 4, Geophone Rock, the ALSEP Central Station, and the Lunar Roving Vehicle. Image ID: AS17-147-22528.
      -Scientific objectives of the Apollo 17 mission included geological surveying and sampling of materials and surface features in a preselected area of the Taurus-Littrow region, deploying and activating surface experiments, and conducting inflight experiments and photographic tasks during lunar orbit and trans-Earth coast (TEC). These objectives were satisfied on Apollo 17 by performance of scheduled science activities, which included 12 lunar surface experiments, 5 lunar orbital experiments, photographic and support tasks, and other experiments.
        The individual Apollo 17 experiments and photographic tasks were as follows:
          Lunar surface:
            Deployed experiments
              Apollo Lunar Surface Experiments Package (ALSEP) - Each ALSEP experiment was connected by a cable to the ALSEP central station, which provided radio communication to Earth and electrical power from a radioisotope thermal generator.
                Heat flow
                Lunar seismic profiling (LSP)
                Lunar surface gravimeter (LSG)
                Lunar atmospheric composition experiment (LACE)
                Lunar ejecta and meteorites (LEAM)
              Surface electrical properties (SEP)
              Lunar neutron probe
              Traverse gravimeter
              Cosmic ray detector
            Sampling
              Lunar geological investigation
              Special samples
            Soil mechanics
          Lunar orbital:
            In addition to their studies on the lunar surface, the Apollo 17 crew performed intensive studies of the Moon from lunar orbit. Along with photography performed with hand-held cameras in the Command Module, a series of experiments were carried in the Scientific Instrument Module (SIM) on the Service Module.
            Orbital experiments
              Lunar sounder
              Infrared (IR) scanning radiometer
              Far ultraviolet (UV) spectrometer
              S-band transponder
              Sodium iodide (Nal) scintillation crystal
            Photographic and support tasks
              Service module (SM) orbital photographic tasks
              Command module (CM) photographic tasks
              Visual observations from lunar orbit
          Other:
            Biomedical experiments
              Biostack II
              BIOCORE
              Visual light flash phenomenon
            Heat flow and convection demonstration
            Apollo window meteoroid
-More info: https://www.history.nasa.gov/alsj/a17/as17psr.pdf

## Slide 14: Surface Experiments on the Moon
On the Moon
Surface experiments
  Surface Electrical Properties
  Lunar Neutron Probe
  Traverse Gravimeter
  Cosmic Ray Detector
Notes: -Image credit: NASA  Jack Schmitt’s pan from Station 8 during EVA-3. Gene Cernan is bending his knees so he can pick up the traverse gravimeter and put it on the back of the rover. Image ID: AS17-142-21730.
      -Deployed Apollo 17 lunar surface experiments:
                Surface Electrical Properties (SEP): This experiment was used to explore the subsurface materials of the Apollo 17 landing site by means of electromagnetic radiation. The characterization of the electrical properties of the lunar regolith (lunar soil) were important for interpreting remote sensing measurements of the Moon such as radar and microwave sounders.
  Lunar Neutron Probe: Designed to obtain a direct in situ (in its original place) measurement of neutron capture rates as a function of depth in the regolith.
  Traverse Gravimeter: A unique experiment carried on Apollo 17. Its primary goal was to make relative gravity measurements at a number of sites in the Apollo 17 landing area and to use these measurements to obtain information about the geological substructure of the Moon.
  Cosmic Ray Detector: Had the following objectives - (1) to measure flux of solar wind particles with atomic number Z > 26 using mica detectors, (2) to determine the flux of light rare gas solar wind ions using metal foils, (3) to measure the flux of low energy particles in space, both solar and galactic, during quiet sun conditions using plastic, glass, and mica detectors, and (4) to determine the radon concentration in the lunar atmosphere using mica detectors.
-More info: https://www.history.nasa.gov/alsj/a17/as17psr.pdf

## Slide 15: Apollo Lunar Surface Experiment Package
Apollo Lunar Surface Experiments Package (ALSEP)
Heat Flow
Lunar Seismic Profiling
Lunar Surface Gravimeter
Notes: -Image credit: NASA  The Lunar Seismic Profiling experiment antenna on the heat flow pallet is shown in the foreground with the Lunar Surface Gravimeter just beyond it. Image ID: AS17-136-20705.
      -Deployed Apollo 17 lunar surface experiments:
                Apollo Lunar Surface Experiments Package (ALSEP) - Each ALSEP experiment was connected by a cable to the ALSEP central station, which provided radio communication to Earth and electrical power from a radioisotope thermal generator.
                Heat Flow: Objectives were to make a direct measurement of the vertical component of heat flow from the lunar interior through the surface and to determine the thermal properties of the upper 3 m of the lunar regolith.
                The deployment of a second heat flow experiment on the lunar surface as a part of the Apollo 17 ALSEP allowed comparison of lunar heat flow measured at two different stations, the Apollo 15 and 17 landing sites. Both Apollo 17 probes were successfully inserted to their full depth of 2.36 m.
                Lunar Seismic Profiling (LSP): Purpose was to record the vibrations of the lunar surface as induced by explosive charges, by the thrust of the lunar module’s ascent engine, and by the crash of the lunar module ascent stage.
                This was an extension of the active seismic experiment carried on the Apollo 14 and 16 missions.
                Lunar Surface Gravimeter (LSG): Designed to make very accurate (1 part in 1011) measurements of the acceleration of lunar gravity and its variation with time.
                Lunar Atmospheric Composition Experiment (LACE): This mini mass spectrometer was designed to identify the various gases in the thin lunar atmosphere (exosphere) and to determine the concentration of each species.
                Lunar Ejecta and Meteorites (LEAM): Objectives were to detect secondary particles that had been ejected by meteorite impacts on the lunar surface and to detect primary micrometeorites themselves.
                The microparticles encountered by the LEAM experiment can be divided into 3 distinct classes: lunar ejecta, interstellar grains, and cometary debris.
-More info: https://www.history.nasa.gov/alsj/a17/as17psr.pdf

## Slide 16: Apollo Lunar Surface Experiment Package
Apollo Lunar Surface Experiments Package (ALSEP)
Lunar Atmospheric Composition Experiment
Lunar Ejecta and Meteorites
Notes: -Image credit: NASA  A pan at the ALSEP site. The Lunar Atmospheric Composition Experiment (LACE) is in view. Image ID: AS17-147-22578.
      -Deployed Apollo 17 lunar surface experiments:
                Apollo Lunar Surface Experiments Package (ALSEP) - Each ALSEP experiment was connected by a cable to the ALSEP central station, which provided radio communication to Earth and electrical power from a radioisotope thermal generator.
                Heat Flow: Objectives were to make a direct measurement of the vertical component of heat flow from the lunar interior through the surface and to determine the thermal properties of the upper 3 m of the lunar regolith.
                The deployment of a second heat flow experiment on the lunar surface as a part of the Apollo 17 ALSEP allowed comparison of lunar heat flow measured at two different stations, the Apollo 15 and 17 landing sites. Both Apollo 17 probes were successfully inserted to their full depth of 2.36 m.
                Lunar Seismic Profiling (LSP): Purpose was to record the vibrations of the lunar surface as induced by explosive charges, by the thrust of the lunar module’s ascent engine, and by the crash of the lunar module ascent stage.
                This was an extension of the active seismic experiment carried on the Apollo 14 and 16 missions.
                Lunar Surface Gravimeter (LSG): Designed to make very accurate (1 part in 1011) measurements of the acceleration of lunar gravity and its variation with time.
                Lunar Atmospheric Composition Experiment (LACE): This mini mass spectrometer was designed to identify the various gases in the thin lunar atmosphere (exosphere) and to determine the concentration of each species.
                Lunar Ejecta and Meteorites (LEAM): Objectives were to detect secondary particles that had been ejected by meteorite impacts on the lunar surface and to detect primary micrometeorites themselves.
                The microparticles encountered by the LEAM experiment can be divided into 3 distinct classes: lunar ejecta, interstellar grains, and cometary debris.
-More info: https://www.history.nasa.gov/alsj/a17/as17psr.pdf

## Slide 17: Exploring the Surface
Notes: -Image credit: NASA  During the first part of the traverse to Station 1 during EVA-1, Gene Cernan drove east about a half kilometer until he got to the east end of three overlapping craters collectively called Trident. He then turned south and stopped to check the map. Jack Schmitt took this picture toward Bear Mountain. The southern end of the East Massif is in the distance. Image ID: AS17-136-20728.
-During the first extravehicular activity (EVA), Gene Cernan and Jack Schmitt offloaded and deployed the Lunar Roving Vehicle (LRV). Following an LRV test drive, the crew gathered samples and performed panoramic photography. They then deployed the U.S. flag and offloaded the ALSEP.
  EVA-1 lasted 7 hours and 12 minutes, with a distance traveled in the LRV of roughly 3 km (2 mi).
-During the second EVA, the astronauts deployed 3 explosive packages for the Lunar Seismic Profiling experiment, made 7 traverse gravimeter measurements, gathered numerous samples, and completed their 500 mm and panoramic photographic tasks.
  They also found orange-colored soil that was of volcanic origin at Station 4 (Shorty Crater).
  EVA-2 lasted 7 hours and 37 minutes, with a distance traveled in the LRV of roughly 20.1 km (12.5 mi).
-During the third and final EVA, specific sampling objectives were accomplished, 9 traverse gravimeter measurements were made, as well as some additional 500 mm and panoramic photography.
  The Surface Electrical Properties experiment was terminated because the receiver temperature was increasing to a level that could have affected the data tape. Consequently, the tape recorder was removed on the way back to the LM.
  EVA-3 lasted 7 hours and 15 minutes, with a distance traveled in the LRV of 12 km (7.5 mi).
  At the end of the final EVA, the astronauts unveiled a plaque on the LM and read it on TV, “Here man completed his first exploration of the Moon, December 1972 A.D. May the spirit of peace in which he came be reflected in the lives of all mankind.”
  The EVA ended with Gene Cernan taking the final step off the lunar surface.
-More info: https://history.nasa.gov/SP-4029/Apollo_17a_Summary.htm
-Apollo 17 Lunar Surface Journal: https://www.hq.nasa.gov/alsj/a17/a17.html

## Slide 18: Orange Soil
Volcanic Moon glass
Ronald Wells/Tranquillity Enterprises
Notes: -Image credits:
  Left: NASA  Orange and black glass spheres that originated in lava fountains on the Moon. These have typical sizes of 20-45 microns. Image ID: S73-15171.
  Right: Ronald Wells/Tranquillity Enterprises  Gene Cernan took this photo at the Station 4 trench during EVA-2 which shows the orange soil at the rim of Shorty Crater. The gnomon, a geology tool used during documentation photographs, is standing at the left.
    Color-balanced derivative of NASA photo AS17-137-20990. Color layers within the original image have been contrast-balanced and adjusted so as to match Jack Schmitt’s initial descriptions, as the original prints and digital scans of the films didn’t properly bring out the colors described.
-During EVA-2, while exploring Shorty Crater, the crew discovered orange-colored soil.
  Jack Schmitt provided an explanation of the surprise discovery in the Apollo Lunar Surface Journal:
    “The reason that this was a little more exciting than it might have even been otherwise was that, in our thinking about the origins of Shorty, we really had two major possibilities, with a number of observations related to each one.
      Number one was what we really believed and what turned out to be true: that Shorty was an impact crater that had penetrated the light mantle and was exposing the dark-mantle and/or subfloor basalt beneath.
      The other alternative, just because of the lack of resolution and information from the pre-mission photographs, was that it was a dark-haloed volcanic crater; and, if that were true, one of the things that we had on our list to look for were signs of alteration, possible fluid-induced alteration of materials around the crater. And normally, on Earth, that alteration is colored, fumarolic alteration from oxidation. And so, when we saw orange, that was the immediate thought that everybody had. 'My God, there's a volcanic emanation here that's altered the soil.' Well, it turned out that that wasn't true, of course.
        It was volcanic material, but it was volcanic glass that had been spewed out of some fire-fountain-like eruptions 3.5 billion years ago that somehow had been protected from mixing with anything else, even though it was now at the surface. It had almost certainly been covered almost immediately by a lava flow, so that it was protected from meteor disruption and stirring.
        And then, when Shorty formed, somehow the pyroclastic ended up in the rim and a few other places in nearly pure form.”
-Commentary from the Apollo Lunar Surface Journal: https://www.hq.nasa.gov/alsj/a17/a17.sta4.html
-More info: https://curator.jsc.nasa.gov/lunar/lsc/74220.pdf
-Apollo 17 in Real Time: https://apolloinrealtime.org/17/?t=145:26:22

## Slide 19: Apollo Lunar Surface Experiment Package
Lunar Sample Collection
Notes:       -Image credit: NASA  Gene Cernan’s Station 1 pan during EVA-1 shows Jack Schmitt shaking soil out of the rake after making a pass through the surface soil. Image ID: AS17-134-20425.
      -A variety of tools were used to collect samples on the Moon’s surface: these included drills, hammers, rakes, tongs, and core tubes.
        -More info on Apollo lunar surface geological sampling tools: https://curator.jsc.nasa.gov/lunar/catalogs/other/jsc23454toolcatalog.pdf

## Slide 20: Apollo Lunar Surface Experiment Package
Sample Core Tubes
Notes:       -Image credit: NASA  The double core tube that Gene Cernan drove into the soil at Station 6 during EVA-3. Image ID: AS17-146-22291.
      -Core tubes were used to obtain samples from below the Moon’s surface using the Apollo Lunar Surface Drill (Apollos 15-17).
      -Two styles of core tubes were used on the Moon to obtain continuous soil columns down to 70 cm in depth.
        The initial style, used on Apollos 11, 12, & 14, was a thick-walled, small diameter (2 cm) tube called a core tube. This tube was designed to be easily opened in the laboratory; however, the soil column obtained in this type of tube was disturbed by the collection process.
        Therefore, a wider diameter (4 cm) tube with thinner walls was designed and fabricated for the last three missions (Apollos 15, 16, & 17). This tube was called a drive tube to distinguish it from the earlier core tube (both tubes took cores and both tubes were driven into the lunar regolith). A soil column collected in a drive tube was not significantly distorted by the coring process.
        -More info on Apollo lunar surface geological sampling tools: https://curator.jsc.nasa.gov/lunar/catalogs/other/jsc23454toolcatalog.pdf
        -Info about the Apollo 17 deep drill core: https://curator.jsc.nasa.gov/lunar/lsc/70009.pdf

## Slide 21: Apollo Lunar Surface Experiment Package
Three-Meter-Deep Drill Core
Notes:       -Image credit: NASA  There are no photos of the crew taking the Apollo 17 deep drill core, but this photo of the site, with the neutron probe in place, shows the effort that was expended to obtain the three-meter-deep drill core. The ALSEP site is just beyond. Image ID: AS17-134-20505.
      -The Apollo 17 deep drill core was collected with great difficulty at the ALSEP site near Camelot Crater and within an area of many small craters known as the Central Cluster. Drilling the
      lowest 20 cm was very difficult, because the bottom material was very cohesive (“sticky”).
        The drill core “string” for Apollo 17 was broken down and returned in three segments (70009, 70008, 70007) (70006, 70005) and (70004, 70003, 70002, 70001) in a special beta-cloth bag. When the drill string was returned to NASA’s Johnson Space Center, a small amount was extracted from the tops of the bottom six segments, and these samples were put in a freezer to preserve them for future study.
        The drill core is a continuous section of the top of the lunar regolith, 3 meters long (a record!), that is providing new insights into the history of the Sun as well as the evolution of the lunar regolith.
          The data from the Apollo 17 deep drill core has been studied in detail by numerous scientists who agree that the top 22 cm of the core sample has been gardened (stirred and mixed) by micrometeorite bombardment.
          A layer at about 240 cm within the drill core was found to indicate an ancient exposure to the Sun, so there have been multiple periods of long exposure to the Sun intermixed with layers of new deposition from impact events.
        -More info: https://curator.jsc.nasa.gov/lunar/lsc/70009.pdf

## Slide 22: Lunar Roving Vehicle (LRV)
Longest LRV traverse on a single extravehicular activity
Notes: -Image credit: NASA  Jack Schmitt took this picture as Gene Cernan approached him on the Lunar Roving Vehicular during its initial test drive during the first extravehicular activity (EVA-1). Note the dust being thrown up by the right-front wheel, even at very low speed. Image ID: AS17-147-22526.
-Apollo 17 saw the third and final flight of the Lunar Roving Vehicle (LRV). With the Lunar Roving Vehicle, total surface traverses increased from hundreds of meters during earlier missions to tens of kilometers during Apollos 15, 16 and 17. Astronauts were thus able to venture farther from the Lunar Module (LM).
  On Apollo 17, the vehicle traversed about 35 km in 4 hours and 29 minutes of driving.
  The longest LRV traverse (20.1 km or 12.5 mi) on a single EVA occurred during Apollo 17. This happened during EVA-2 which lasted 7 hours and 37 minutes.
    The farthest the LRV reached from the LM was 4.74 mi (7.63 km).
-The empty weight of the rover was 462 lb (210 kg) on Earth and only 77 lb (35 kg) on the Moon, so the astronauts could use the U-shaped handles on the outer edges of the vehicle to lift and reposition the rover.

## Slide 23: Lee Lincoln scarp
Notes: -Video credit: NASA’s Scientific Visualization Studio  An animated view of Lee Lincoln scarp from above and from near ground level. This visualization is created from Lunar Reconnaissance Orbiter photographs and elevation mapping.
  The Apollo 17 astronauts drove their lunar rover onto the scarp during their second day on the lunar surface, and this remains the only extraterrestrial scarp visited by humans.
-The Lee Lincoln scarp is a low ridge or step about 80 meters high and running north-south through the western end of the Taurus-Littrow valley.
  This lobate scarp marks the location of a relatively young, low-angle thrust fault. The land west of the fault was forced up and over the eastern side as the lunar crust contracted.
  In a May 2019 paper published in Nature Geoscience (http://dx.doi.org/10.1038/s41561-019-0362-2), scientists provide evidence that this fault and others like it are still active and producing moonquakes today.
    Seismometers left on the Moon by Apollo astronauts recorded hundreds of events between 1969 and 1977, including 28 shallow moonquakes.
    The study narrowed the locations of these quakes and found that many of them occurred near scarps, implying that the forces creating the scarps also caused the quakes, and they continue to shape the lunar surface.
    The Lee Lincoln scarp was only about 13 kilometers from one of the epicenters identified by the scientists.
-Video source: https://svs.gsfc.nasa.gov/4714

## Slide 24: Singing on the Moon
121:35:45 Schmitt: (Singing) I was strolling on the Moon
one day...
121:35:49 Lunar Module Crew: (Both singing)...in the
merry, merry month of
121:35:51 Schmitt: December.
121:35:52 Cernan: No, May.
121:35:54 Schmitt: May.
121:35:55 Cernan: May’s the month this year.
Notes: -Image credits: NASA
-Transcript between astronauts and Houston Mission Control (times are elapsed time after launch) during EVA-1:
121:35:45 Schmitt: (Singing) I was strolling on the Moon one day...
121:35:49 Lunar Module Crew: (Both singing)...in the merry, merry month of
121:35:51 Schmitt: December.
121:35:52 Cernan: No, May.
121:35:54 Schmitt: May.
121:35:55 Cernan: May’s the month this year.
121:35:56 Schmitt: May. That's right.
121:35:57 Cernan: May is the year of the month.
121:36:00 Schmitt: (Singing) When much to my surprise, a pair of bonny eyes...be-doop-doo-doo...
121:36:05 Parker: Sorry about that, guys, but today may be December. (Bob Parker was the EVA CapCom for Apollo 17)
121:36:08 Cernan: Okay, the battery cover...
121:36:13 Schmitt: (Humming) Da-da-da-da-da-da-da-dee-da-dee...
[The song "While Strolling through the Park One Day" was written by Ed Haley in 1884.]
-Source: Eric M. Jones; https://www.hq.nasa.gov/alsj/a17/a17.trvsta1.html
-Apollo 17 in Real Time: https://apolloinrealtime.org/17/?t=121:35:43

## Slide 25: Singing on the Moon
121:35:56 Schmitt: May. That's right.
121:35:57 Cernan: May is the year of the month.
121:36:00 Schmitt: (Singing) When much to my surprise,
a pair of bonny eyes...be-doop-doo-doo...
121:36:05 Parker: Sorry about that, guys, but today
may be December.
121:36:08 Cernan: Okay, the battery cover...
121:36:13 Schmitt: (Humming) Da-da-da-da-da-da-da
dee-da-dee...
Notes: -Image credits: NASA
-Transcript between astronauts and Houston Mission Control (times are elapsed time after launch) during EVA-1:
121:35:45 Schmitt: (Singing) I was strolling on the Moon one day...
121:35:49 Lunar Module Crew: (Both singing)...in the merry, merry month of
121:35:51 Schmitt: December.
121:35:52 Cernan: No, May.
121:35:54 Schmitt: May.
121:35:55 Cernan: May’s the month this year.
121:35:56 Schmitt: May. That's right.
121:35:57 Cernan: May is the year of the month.
121:36:00 Schmitt: (Singing) When much to my surprise, a pair of bonny eyes...be-doop-doo-doo...
121:36:05 Parker: Sorry about that, guys, but today may be December. (Bob Parker was the EVA CapCom for Apollo 17)
121:36:08 Cernan: Okay, the battery cover...
121:36:13 Schmitt: (Humming) Da-da-da-da-da-da-da-dee-da-dee...
[The song "While Strolling through the Park One Day" was written by Ed Haley in 1884.]
-Source: Eric M. Jones; https://www.hq.nasa.gov/alsj/a17/a17.trvsta1.html
-Apollo 17 in Real Time: https://apolloinrealtime.org/17/?t=121:35:43

## Slide 26: Lunar Poet
“It's the week before Christmas And all through the LM, Not a commander was stirring, Not even Cernan. The samples were stowed in their places with care, In hopes that with you, they soon will be there. And Gene in his hammock and I in my cap, Had just settled our brains for a short lunar nap. But up on the comm loop there rose such a clatter, I sprang from my hammock, to see what was the matter. The Sun on the breast of the surface below, Gave the luster of objects, as if in snow. And what to my wondering eyes should appear, But a miniature Rover and eight tiny reindeer. And a little old driver so lively and quick, I knew in a moment; it must be St. Nick. I heard him exclaim as over the hills he did speed. Merry Christmas to all and to you all Godspeed.”
-Apollo 17 Astronaut Jack Schmitt
Notes: -Image credit: NASA  Gene Cernan took this photo of Jack Schmitt after they were out of their suits after EVA-3. Image ID: AS17-134-20530.
-Transcript between astronauts and Houston Mission Control (times are elapsed time after launch), while Cernan & Schmitt were waiting to depart from the Moon:
183:36:46 Schmitt: Hey, Gordy. In honor of one of your comm handovers last night, and in the tradition of Apollo 8, I’ve got a paraphrase of a familiar poem for you.
183:37:01 Fullerton: Okay; go ahead.
183:37:03 Schmitt: Well,
“It’s the week before Christmas And all through the LM, Not a commander was stirring, Not even Cernan. The samples were stowed in their places with care, In hopes that with you, they soon will be there. And Gene in his hammock and I in my cap, Had just settled our brains for a short lunar nap. But up on the comm loop there rose such a clatter, I sprang from my hammock, to see what was the matter. The Sun on the breast of the surface below, Gave the luster of objects, as if in snow. And what to my wondering eyes should appear, But a miniature Rover and eight tiny reindeer. And a little old driver so lively and quick, I knew in a moment; it must be St. Nick. I heard him exclaim as over the hills he did speed. Merry Christmas to all and to you all Godspeed.”
183:38:22 Fullerton: Very good.
183:38:27 Cernan: Gordo, that was the first time I heard that, and I got to say that is beautiful!
183:38:33 Fullerton: I agree. Did the LMP get any sleep, or did he spend all night composing that?
183:38:43 Cernan: People always said we ought to have a poet in space.
-Source: Eric M. Jones; https://www.hq.nasa.gov/alsj/a17/a17.launch.html
-Apollo 17 in Real Time: https://apolloinrealtime.org/17/?t=183:36:46

## Slide 27: From the Earth to the Moon
Notes: -Image credit: NASA  This portrait of Jack Schmitt with the U.S. flag and the Earth was taken by Gene Cernan during EVA-1 near the LM. Image ID: AS17-134-20384.

## Slide 28: Flight of the Geology Hammer
Notes: -Image credit: NASA  At the end of the last EVA, Jack Schmitt threw the crew’s geology hammer off into the distance. This is the first of several images that Gene Cernan took to document the flight of the geology hammer. Image ID: AS17-143-21938.
-More info: https://www.hq.nasa.gov/alsj/a17/a17.hammer.html ; https://www.hq.nasa.gov/alsj/a17/a17-HammerFlight.html
-Apollo 17 in Real Time: https://apolloinrealtime.org/17/?t=170:29:45

## Slide 29: Apollo 12 Traverses
Notes: -Image source: https://www.lpi.usra.edu/publications/slidesets/apollolanding/ApolloLanding/slide_37.html
-The Apollo 17 traverses.
  The thick lines indicate the paths taken by the astronauts during the three EVAs.
  Numbered spots indicate sampling stations along the individual traverses.
  Spots labeled LRV involved photography and sampling from the Lunar Roving Vehicle.
-The diagram is based on the Apollo 17 Traverses Lunar Photomap, Edition 1, Sheet 43D1S2[25].

## Slide 30: Apollo 12 landing site, as imaged by the Lunar Reconnaissance Orbiter Camera
Notes: -Image credit: NASA’s Scientific Visualization Studio  https://svs.gsfc.nasa.gov/4717
-This visualization of the Taurus-Littrow valley, site of the Apollo 17 Moon landing, uses multiple Lunar Reconnaissance Orbiter datasets to zoom into the valley and illustrate the paths taken by the astronauts during their three days of exploration at the site.
  The data includes wide-angle camera (WAC) and narrow-angle (NAC) camera images, LOLA laser altimetry, and a high-resolution elevation map created from NAC stereo pairs.
  The imagery was chosen to approximately match the lighting conditions at the time of the landing.
  Color-coded trails with numbered stops (called stations in astronaut lingo) show where Eugene Cernan and Jack Schmitt drove their lunar rover - orange on day 1, blue on day 2, and green on day 3.
-More info: http://lroc.sese.asu.edu/posts/72

## Slide 31: Apollo 17 Traverses
Apollo 17 Traverses  New York City
NASA/GSFC/Brent Garry
Notes: -Image credit: NASA/GSFC/Brent Garry
-Apollo 17 tracks overlain on New York City, NY.

## Slide 32: Apollo 12 landing site, as imaged by the Lunar Reconnaissance Orbiter Camera
Notes: -Video credit: NASA’s Scientific Visualization Studio  https://svs.gsfc.nasa.gov/4717
-This visualization of the Taurus-Littrow valley, site of the Apollo 17 Moon landing, uses multiple Lunar Reconnaissance Orbiter datasets to zoom into the valley and illustrate the paths taken by the astronauts during their three days of exploration at the site.
  The data includes wide-angle camera (WAC) and narrow-angle (NAC) camera images, LOLA laser altimetry, and a high-resolution elevation map created from NAC stereo pairs.
  The imagery was chosen to approximately match the lighting conditions at the time of the landing.
  Color-coded trails with numbered stops (called stations in astronaut lingo) show where Eugene Cernan and Jack Schmitt drove their lunar rover - orange on day 1, blue on day 2, and green on day 3.

## Slide 33: Mission Plaque
Notes: -Image credits: NASA
  Left: A photographic replica of the plaque left on the Moon by the crew of Apollo 17.
  Right: Gene Cernan next to the LM during EVA-3. Notice the commemorative plaque in between two rungs of the LM ladder.
-At the end of the final EVA, the astronauts unveiled a plaque on the LM and read it on TV, “Here man completed his first exploration of the Moon, December 1972 A.D. May the spirit of peace in which we came be reflected in the lives of all mankind.”

## Slide 34: Farewell, Moon
Notes: -Video source: NASA  The Apollo 17 lunar module ascent stage lifting off from the Moon’s surface on December 14, 1972, with Gene Cernan and Jack Schmitt onboard. https://history.nasa.gov/alsj/a17/video17.html#launch
-YouTube video from the National Air and Space Museum: https://www.youtube.com/watch?v=9HQfauGJaTs
-More info: https://www.hq.nasa.gov/alsj/a17/a17.launch.html

## Slide 35: Returned Samples
Apollo 17 Earthrise
Notes: -Image credit: NASA  Earthrise from lunar orbit during Apollo 17. Image ID: AS17-152-23274

## Slide 36: Surface Experiments on the Moon
Lunar Sounder
Infrared (IR) Scanning Radiometer
Far Ultraviolet (UV) Spectrometer
S-band Transponder
Sodium Iodide (Nal) Scintillation Crystal
Orbital Science Experiments
Notes:       -Image credit: NASA  A cartoon illustrating the operation of the Lunar Sounder. Image ID: S72-53472.
      -In addition to their studies on the lunar surface, the Apollo 17 crew performed intensive studies of the Moon from lunar orbit. Along with photography performed with hand-held cameras in the Command Module, a series of experiments were carried in the Scientific Instrument Module (SIM) on the Service Module.
        Orbital experiments
          Lunar Sounder: Designed to (1) map the subsurface electrical conductivity structure to infer geological structure, (2) make surface profiles to determine lunar topographic variations, (3) produce surface imaging, and (4) measure galactic electromagnetic radiation in the lunar environment.
          Infrared (IR) Scanning Radiometer: Measured the thermal emission coming from the lunar surface in order to obtain a high-resolution surface temperature map.
          Far Ultraviolet (UV) Spectrometer: Primary purpose was to make measurements from orbit of the ultraviolet emissions from the tenuous lunar atmosphere.
            It also had secondary objectives to make non-lunar observations during lunar orbit and trans-Earth coast, including zodiacal light, solar atmosphere emissions, Earth emissions (including those from the geomagnetic tail), stellar emissions, and galactic emissions.
          S-band Transponder: Purpose was to measure the lunar gravitational field, which in turn provided information on the lunar mass distribution and its correlation with surface features.
            An estimate derived from these observations for the value of lunar gravity at the landing site compared very well with that obtained by the lunar traverse gravimeter.
          Sodium Iodide (Nal) Scintillation Crystal: To obtain experimental data on the extent of cosmic-ray -induced activity during spaceflight, a sodium iodide (thallium-activated) (Nal(Tl)) crystal was flown onboard the Apollo 17 command module.
        Photographic and support tasks
          Service module (SM) orbital photographic tasks
          Command module (CM) photographic tasks
          Visual observations from lunar orbit
      -More info: https://www.history.nasa.gov/alsj/a17/as17psr.pdf

## Slide 37: Surface Experiments on the Moon
Biomedical
Heat Flow and Convection Demonstration
Apollo Window Meteoroid
Other Experiments
Notes: -Image credit: NASA  Diagonal view of the heat flow experiment onboard the command module, with the convection pattern visible in the left-hand cell. Image ID: AS17-162-24063.
      -In addition to lunar surface and orbital experiments, the Apollo 17 astronauts performed “other” experiments, including:
        Biomedical experiments
          Biostack II: Purpose was to study the effects of individual heavy nuclei of galactic cosmic radiation on biologic specimens during spaceflight outside of the magnetosphere of the Earth.
          BIOCORE: Objective was to determine if heavy cosmic ray particles (stripped nuclei) injure the brain, eyes, skin, and other tissues. The experiment consisted of a group of pocket mice with cosmic ray detectors planted under their scalps which were flown aboard the Apollo 17 command module in a special container.
          Visual light flash phenomenon: Apollo 17 was the fourth mission during which an investigation of the so-called light flash phenomenon was conducted. During Apollos 14 and 15, 1-hr observing sessions were designated for the crewmen to darken the cabin (blindfolds used on Apollo 15) and to look for the phenomena.
            Their observations were reported in real time. The Apollo light flash moving emulsion detector (ALFMED) flown on Apollo 16 provided the first opportunity to record the passage of cosmic rays through the crewman’s head and eyes and to correlate them with his observations.
            Because the crewmen are exposed to cosmic rays and because ionizing radiation has been demonstrated to be capable of producing the same type of effect, the most probable explanation of the phenomenon is that it is caused by cosmic rays penetrating the eyes and retinas of the observers.
        Heat Flow and Convection demonstration: Experiments conducted in the command module by Ronald Evans showed that in uncovered liquids, convection driven by surface tension can occur at lower temperature gradients in low gravity (about 10-8g) than in 1g. In completely confined fluids (no liquid-gas interface), vibrations caused by spacecraft and astronaut movements increased the heat transfer considerably over the pure conduction case. https://www.science.org/doi/10.1126/science.187.4172.165
        Apollo Window Meteoroid experiment: Objective was to use the Apollo 17 command module heat shield window surfaces (fused silica) to obtain information about the flux of meteoroids with masses of 1 nanogram or less.
      -More info: https://www.history.nasa.gov/alsj/a17/as17psr.pdf ; https://nssdc.gsfc.nasa.gov/planetary/lunar/apollo17info.html

## Slide 38: Surface Experiments on the Moon
S-IVB Rocket Stage Impact Site
NASA/GSFC/Arizona State University
Notes: -Image credit: NASA/GSFC/Arizona State University  The Lunar Reconnaissance Orbiter (LRO) captured this image of the impact site of the Apollo 17 S-IVB stage. http://www.lroc.asu.edu/featured_sites/view_site/27
  S-IVBs were portions of the Saturn V rockets that brought astronauts to the Moon.
  Beginning with Apollo 13, the S-IVB rocket stages were deliberately impacted on the lunar surface after they were used.
    Seismometers placed on the Moon by the Apollo astronauts measured the energy of these impacts to shed light on the Moon’s internal structure.
  The third stage of the Apollo 17 Saturn V launch vehicle was intentionally impacted on the lunar surface on December 10, 1972.
    The impact left a 31-meter diameter crater.

## Slide 39: By the Numbers
Deep Space Space Walk
Notes: -Image credit: NASA  Apollo 17 command module pilot, Ronald Evans, is photographed performing an extravehicular activity (EVA) during the Apollo 17 spacecraft’s trans-earth coast. During his EVA, Evans retrieved film cassettes from the lunar sounder, mapping camera, and panoramic camera. The cylindrical object at Evans’ left side is the mapping camera cassette. The total time for the trans-earth EVA was 1 hour, 7 minutes, 18 seconds, and took place on December 17, 1972. Image ID: AS17-152-23391.
-More info: https://www.hq.nasa.gov/alsj/a17/a17.homeward.html

## Slide 40: Splashdown
Splashdown
Notes: -Image credits: NASA
  Left: The Apollo 17 command module America just before splashdown. Image ID: S72-55834.
  Right: The first of the crewmembers is winched up to the recovery helicopter while the other two wait in the raft with Navy divers. The recovery ship, the USS Ticonderoga, is in the background. Image ID: S72-55974.
-The Apollo 17 splashdown occurred on December 19, 1972, in the Pacific Ocean.

## Slide 41: Splashdown
Apollo Moon Cake!
Notes: -Image credits: NASA
  Left: The Apollo 17 recovery dinner cake. Image ID: S72-56068.
  Right: The Apollo 17 astronauts prepare to cut the recovery cake onboard the USS Ticonderoga. Image ID: S72-56081.

## Slide 42: Returned Samples
Returned Samples
Notes: -Image credits: NASA
  Left: Apollo 17 rake sample 76535,6. Classified as a Troctolite, it appears almost gem-like due to its atypical luster and color (unusual compared to the rest of the Apollo Lunar Collection) and has a unique crystalline structure consisting almost entirely of large grains of homogeneous olivine and plagioclase in near equal quantities. Image ID: S73-19596.
  Right: Apollo 17 sample 70017. This rock is classified as a high-titanium basalt and is highly vesicular, containing many visible voids, which are now the empty chambers of ancient gas bubbles, illustrating this rock’s volcanic origin. Thought to be the very last rock to be picked up on the Moon by the Apollo missions, it is now known as the Children of the World rock. Collected as a good will rock to be shared with every country of that era, it was meant to honor and celebrate the children who would be the future hope of exploration and peaceful collaboration among nations. 70017 was subdivided and presented to the leaders of 135 countries and all 50 U.S. states. Image ID: S73-15723.
  -The Apollo 17 crew collected 741 individual rock and soil samples, including a deep drill core with material from 3 meters below the lunar surface, with a total mass of roughly 243 pounds (110 kilograms).
  -The overall set of lunar samples collected during the Apollo program can be classified into 3 major rock types: basalts, breccias (rocks that are composed of fragments of other, older rocks), and highland crustal rocks. Apollo 17 collected important examples of all three rock types.
    Rocks from the floor of the Taurus-Littrow valley are mostly mare basalts. Basalt consists primarily of the minerals plagioclase and pyroxene and is formed from molten lava.
    The Serenitatis basin formed from the impact of a large asteroid or comet with the Moon. The Taurus Mountains surrounding the Apollo 17 landing site were pushed up by this impact. Impact breccias from the younger Imbrium basin impact were later deposited on top of the Taurus Mountains.
      Many of the rocks from the South Massif landslide at Stations 2 and 3 and from the boulders that rolled down the North Massif at Stations 6 and 7 are impact melt breccias from one of these two large impact events.
    The Apollo 17 astronauts also collected several rare types of lunar rock, including norite, troctolite, and dunite. Norite consists primarily of the minerals plagioclase and orthopyroxene. Troctolite consists primarily of plagioclase and olivine, and dunite is nearly pure olivine.
      Many of these rocks originally formed in the lower half of the Moon’s crust during the solidification of the Moon’s magma ocean. These rocks formed between 4.2 and 4.5 billion years ago (the solar system formed about 4.56 billion years ago). They were later brought to the Moon’s surface by large asteroid impacts, such the impact that formed the Serenitatis basin.
  -More info: https://www.lpi.usra.edu/lunar/missions/apollo/apollo_17/samples/
  -Apollo 17 sample catalog: https://www.hq.nasa.gov/alsj/a17/a17sampcat.html
  -JSC Lunar Sample Compendium: https://curator.jsc.nasa.gov/lunar/lsc/index.cfm
  -Explore some of the Apollo 17 samples with Astromaterials 3D: https://ares.jsc.nasa.gov/astromaterials3d/sample-catalog.htm?origin=A17

## Slide 43: Apollo Next Generation Sample Analysis Program
NASA/James Blair
Notes: -Image credit: NASA/James Blair  Pictured from left: Apollo sample processors Andrea Mosie, Charis Krysher and Juliane Gross open Apollo 17 lunar sample 73002 at NASA’s Johnson Space Center.
-Lunar sample 73002 was opened on Nov. 5, 2019, in the Lunar Curation Laboratory at NASA’s Johnson Space Center. It had been collected on the Moon by Apollo 17 astronauts Gene Cernan and Jack Schmitt, who drove a 4-centimeter-wide tube into the surface of the Moon to collect it. The sample was opened as part of NASA’s Apollo Next Generation Sample Analysis (ANGSA) initiative, which is leveraging advanced technologies to study Apollo samples using new tools that were not available when the samples were originally returned to Earth.
-Since the Apollo era, all samples that were returned to Earth have been carefully stored in the laboratory to preserve them for future generations. Most samples have been well studied, and many are the subject of ongoing research.
  However, NASA also made the decision to keep some samples completely untouched as an investment in the future, allowing them to be analyzed with more advanced technologies as they are developed.
    These include samples that remained sealed in their original containers, as well as some stored under special conditions, all intended to be opened and analyzed with more advanced analytical technologies than were available during Apollo.
    The unopened Apollo samples were collected on Apollos 15, 16 and 17.
      Two of those samples, 73002 and 73001, both collected on Apollo 17, are being studied as part of ANGSA.
        This research is helping us to prepare for returning humans to the Moon as part of NASA’s Artemis missions to the Moon’s South Pole.
    Advances in techniques such as non-destructive 3D imaging, mass spectrometry and ultra-high resolution microtomy are allowing for a coordinated study of these samples at an unprecedented scale.
-Nov. 6, 2019: NASA Opens Previously Unopened Apollo Sample Ahead of Artemis Missions  https://www.nasa.gov/feature/nasa-opens-previously-unopened-apollo-sample-ahead-of-artemis-missions
-Dec. 23, 2019: Our Favorite Holiday Gift? A Box of Apollo Moon Soil  https://www.nasa.gov/feature/goddard/2019/the-best-holiday-gift-of-all-50-year-old-moon-soil
-March 4, 2022: NASA Studies ‘New’ 50-Year-Old Lunar Sample to Prep for Return to Moon  https://www.nasa.gov/feature/nasa-studies-new-50-year-old-lunar-sample-to-prep-for-return-to-moon
-May 3, 2022: NASA Goddard Scientists Begin Studying 50-year-old Frozen Apollo 17 Samples  https://www.nasa.gov/feature/goddard/2022/apollo-17-lunar-samples

## Slide 44: By the Numbers
22 hrs, 4 min spent outside the lander
22 mi (35 km) total length of EVA drive traverses
243 lbs (110 kg) of samples collected
About 302 hrs (~12.6 days) total mission time
By the Numbers
Notes: -Image credit: NASA  Apollo 17 lunar module Challenger’s rendezvous with the command module America. Image ID: AS17-149-22847.
-Farthest point traveled from the lunar module: 4.74 mi (7.63 km)
-Compare to Apollo 11:
  60 m – farthest point traveled from the lunar module (no lunar rover!)
  2.5 hrs spent outside the lunar module
  47.8 lbs of samples collected
  195 hrs, 18 min, 35 sec (~8 days) total mission time

## Slide 45: Apollo 17 Command Module
Name: “America”
Location:
  Space Center Houston, NASA’s Johnson Space Center
  Houston, TX
National Air and Space Museum
Notes: -Image credit: National Air and Space Museum  https://airandspace.si.edu/collection-objects/command-module-apollo-17
-The color of the command module is due to the mylar material used.

## Slide 46: More Info
More Info
Notes: -Image credit: NASA  A panoramic view of the North Massif from Station 1, taken during the first EVA of Apollo 17. Image ID: AS17-134-20430.

## Slide 47: Apollo Landing Sites
Apollo Landing Sites
NASA/GSFC/Arizona State University
Notes: -Image credit: NASA/GSFC/Arizona State University
  Left: Apollo landing sites (lunar near side)
  Right: Lunar far side
(captured by the Lunar Reconnaissance Orbiter spacecraft)

## Slide 48: Apollo 11 Traverses
Apollo 11 Traverses  New York City
NASA/GSFC/Brent Garry
Notes: -Image credit: NASA/GSFC/Brent Garry
-Apollo 11 tracks overlain on the Intrepid Sea, Air & Space Museum in New York City, NY.
-Future Apollo missions would travel up to ~5 mi from the lunar module (Apollo 17).

## Slide 49: Apollo 12 Traverses
Apollo 12 Traverses  Rome
Thomas Schwagmeier
Notes: -Image credit: Thomas Schwagmeier
-The Apollo 12 traverse map superimposed on a simplified map of Rome.
-Note that Surveyor Crater is slightly larger than the Coliseum.
-Source: https://www.hq.nasa.gov/alsj/TraverseMapsEarth.html

## Slide 50: Apollo 12 Traverses
Apollo 14 Traverses  Washington, D.C.
Thomas Schwagmeier
Notes: -Image credit: Thomas Schwagmeier
-Overlay of the Apollo 14 traverse map, derived from high-resolution Lunar Reconnaissance Orbiter Camera images, on a simplified map of Washington D.C.
-With the lunar module placed at the Lincoln Memorial, the center of Cone crater is on E Street between the South Lawn of the White House and the Ellipse.
-Source: https://www.hq.nasa.gov/alsj/TraverseMapsEarth.html

## Slide 51: Apollo 12 Traverses
Thomas Schwagmeier and Eric M. Jones
Apollo 15 Traverses  New York City
Notes: -Image credit: Thomas Schwagmeier and Eric M. Jones
-Overlay of the Apollo 15 traverse map on Manhattan, New York City.
-Because of the Lunar Roving Vehicle, the Apollo 15 crew was able to travel much farther from the lunar module than any of the previous Apollo missions.
-Source: https://www.hq.nasa.gov/alsj/TraverseMapsEarth.html

## Slide 52: Apollo 12 Traverses
Apollo 16 Traverses  Sydney
Thomas Schwagmeier
Notes: -Image credit: Thomas Schwagmeier
-The Apollo 16 traverse map superimposed on a simplified map of Sydney.
-Source: https://www.hq.nasa.gov/alsj/TraverseMapsEarth.html

## Slide 53: JFK’s Speech
The Decision to Go to the Moon
  May 25, 1961
We Choose to Go to the Moon
  September 12, 1962
JFK’s Speech
Notes: -Image source: https://history.nasa.gov/moondec.html  JFK’s address to Congress.
-”The Decision to Go to the Moon”: President John F. Kennedy's May 25, 1961 Speech before Congress. JFK announced before a special joint session of Congress the dramatic and ambitious goal of sending an American safely to the Moon before the end of the decade.
-”We choose to go to the Moon” is the famous tagline of a speech about the effort to reach the Moon delivered by President John F. Kennedy to a large crowd gathered at Rice Stadium in Houston, Texas on September 12, 1962.

## Slide 54: Additional Resources
Apollo Images:
  https://images.nasa.gov/
  https://www.hq.nasa.gov/alsj/a17/images17.html
  http://lroc.sese.asu.edu/featured_sites#ApolloLandingSites
Apollo Videos:
  https://svs.gsfc.nasa.gov/Gallery/apollo.html
Apollo 17 General:
  https://apolloinrealtime.org/17/
  https://nssdc.gsfc.nasa.gov/planetary/lunar/apollo17info.html
  https://www.hq.nasa.gov/alsj/a17/a17.html
  Preliminary Science Report: https://history.nasa.gov/alsj/a17/a17psr.html
Additional Resources